## Slide 1
Contents
Scope 8
  Gas Turbines 8
  Steam Turbines 9
Methodological Notes 10
Vital Statistics 11
Gas Turbines 12
  Market Overview 12
    Demand 12
    Supply (Capacity) 15
    New contracts 19
  Analysis 25
    Costs 25
    Profit Margins 27
  Prices 28
    Price Differences by Technology, Model, and Feature 31
    Should-Cost Analysis 38
  Price Negotiation Strategies 39
Steam Turbines 41
  Market Overview 41
    Demand 41
    Supply (Capacity) 44
    New contracts 48
  Analysis 52
    Costs 52
    Profit Margins 53
  Prices 54
    Price Differences by Technology, Model, and Feature 56
    Should-Cost Analysis 60
1

## Slide 2
5.4 Price Negotiation Strategies 61
Reference product definitions and scope 62
  Gas Turbines 62
  Steam Turbines 62
Notes 63
2

## Slide 3
Table of Figures
Figure 1: Demand for Gas Turbines 14 Figure 2: Capacity Margin – Gas Turbines 16 Figure 3: Demand vs. Capacity – Gas Turbines 17 Figure 4: Cost Structure for Gas Turbines 26 Figure 5: Overall Price Forecast for Gas Turbines 29 Figure 6: Gas Turbine Cost vs. Power Output 35 Figure 7: Gas Turbine Cost Premium per Incremental 1% of Efficiency (Mechanical Drive) 35 Figure 8: Gas Turbine Cost per kW of Generating Capacity 37 Figure 9: Gas Turbines Economies of Scale 38 Figure 10: Should-Cost for Gas Turbines 39 Figure 11: Demand for Steam Turbines 44 Figure 12: Capacity Margin - Steam Turbines 45 Figure 13: Demand vs. Capacity - Steam Turbines 48 Figure 14: Cost Structure for Steam Turbines 52 Figure 15: Overall Price Forecast for Steam Turbines 55 Figure 16: Steam Turbine Cost vs. Power Output by Application and Steam Pressure 59 Figure 17: Steam Turbine Cost per kW Installed 59 Figure 18: Economies of Scale in Steam Turbines 60 Figure 19: Should-Cost for Steam Turbines 61
3

## Slide 4
4
Table of Tables
Table 1: Demand, Order Lead Time, Capacity Utilization, and Prices 11 Table 2: Key Indicators for Gas Turbines 12 Table 3: Reported or Estimated Capacity Utilization Rates at Selected Gas Turbine Suppliers 18 Table 4: Summary of New Contracts and Estimated Values for Gas Turbines 23 Table 5: Regional Price Variations over Time for Gas Turbines 30 Table 6: Incremental Cost per Parameter or Feature for a 25-35 MW Gas Turbine 32 Table 7: Incremental Cost per Parameter or Feature for a 50-85 MW Gas Turbine 33 Table 8: Incremental Cost per Parameter or Feature for a 220-270 MW Gas Turbine 34 Table 9: Key Indicators for Steam Turbines 41 Table 10: Reported or Estimated Capacity Utilization Rates at Selected Steam Turbine Suppliers ... 46 Table 11: Summary of New Contracts and Estimated Values for Steam Turbines 51 Table 12: Regional Price Variations over Time for Steam Turbines Compressors 56 Table 13: Incremental Cost per Extra Parameter or Feature for a 30-70 MW Steam Turbine for
Mechanical Drive 57
Table 14: Incremental Cost per Extra Parameter or Feature for a 100-140 MW Steam Turbine for Combined-Cycle Power Generation 58

## Slide 5
5
Abbreviations
Acfm: Actual cubic feet per minute API: American Petroleum Institute
ASME: American Society of Manufacturing Engineers b: billions
barg: bar gauge Bpd: barrels per day
Bbl: barrel of crude oil BOG: Boil off gas
BTU: British Thermal Unit
Capex: capital expenditure
CCGT: Combined Cycle Gas Turbine Cfm: cubic feet per minute
CHP: Combined Heat and Power Cfm: cubic feet per minute
E&P: Exploration and Production
EPC: Engineering, Procurement, and Construction FPSO: floating production, storage and offloading GPM: gallons per minute
GW: gigawatts k: thousands kW: kilowatts
LTSA: Long Term Service Agreement m: millions
MW: megawatts
M&A: Merger and Acquisition MENA: Middle East and North Africa Mmbtu: one million BTUs
MRO: maintenance, repair and operating

## Slide 6
6
NGL: Natural Gas Liquids
Nm: Newton-meter
PCP: Steam Turbines Pump Psi: pounds per square inch
Psig: pounds per square inch gauge
ROP: Rate of Penetration
Scfm: Standard cubic feet per minute t: trillion
Tonnes=metric tons
Tons: short tons Tpy: tons per year
WTI: West Texas Intermediate crude oil YOY: year over year
YTD: year to date
Alerts:
Yellow Alert
(applies to any time period)
Capacity margin < $150 million per year
Capacity Utilization > 85%
Important news
Red Alert
(applies to next year only)
Prices change 5%+
Capacity margin < $100 million per year
Capacity Utilization > 90%
Chart Symbols:
≡ Stable, ▲= Increasing, ▼ = Decreasing, LO = Low supplier concentration, ► = Moderate supplier concentration, HI= High supplier concentration

## Slide 7
7
1 Scope
This study focuses on Gas- and steam-driven turbines with power ratings ranging from 25-270 MW for gas turbines and 30-140 MW for steam turbines. Applications include driving rotating equipment such as pumps or compressors, and producing power for other operations. Gas turbines are commonly used in field applications (to drive oilfield or pipeline turbomachinery), in refineries to generate both power and heat, and in dedicated power stations. Steam turbines are employed most frequently in applications where there is a ready source of heat to create steam, such as a refinery where processes such as distillation and cracking create heat or a power station, where a gas turbine, boiler, or reactor is used.
1.1 Gas Turbines
Gas turbines are classified by power rating, design, and application.
By power rating, this study addresses the entire range from microturbines (units with output of less than 1 MW – not covered in this study) to machines that produce up to 470 MW of electricity. Power rating requirements at either end, the very small or the very large, can limit a buyer’s choice of manufacturer, and have a substantial impact on unit efficiency (25% for units at the smaller end of the range to as much as 41% for the largest, latest models).
By design, the study addresses both “industrial” and “aero-derivative” turbines. Aero-derivative designs are based on aircraft engines, and are distinguished primarily by being more compact than industrial turbines (30-50% smaller), and also somewhat more efficient (4-10% for turbine models with similar output ranges). As a result, aero-derivatives are common choices on offshore platforms or in locations where costs for space and weight are high. The main manufacturers of aero-derivative units are GE (LM-series) and Rolls Royce (RB211 and Avon).
By application, the study considers both those used for power generation and mechanical drive, although this classification affects the ancillary equipment associated with the turbine more than the engine itself. Many manufacturers offer essentially the same models for both applications, with minor variations. Power generation turbines range from 1-470 MW of electrical output. They are often directly coupled with an electrical generator, which eliminates some of the cost for mechanical power transmission components. Gas turbine models commonly used for mechanical drive typically range from 1.5k hp (1.1 MW) to 175k hp (131 MW).
The study focuses on the turbine itself rather than the entire package, though many buyers opt to purchase gas turbine with ancillary service such as installation and commissioning. Focusing on the turbine itself promote an effective comparison between mechanical drive and power generation units, which are packaged with different components, and to more accurately measure the impact of regional price variations, which can are usually amplified when local components or local packagers are used.
For mechanical drive units, these excluded package components primarily consist of:

## Slide 8
8
Gearbox
Skid
Drive shaft coupling
Intake and exhaust systems
Mechanical auxiliaries
For power generation units, the excluded package components are:
Electric generator
Intake and exhaust systems
Mechanical auxiliaries
Electrical auxiliaries
1.2 Steam Turbines
Steam Turbines can also be used to drive rotating machinery or to generate power, using steam pressure to turn a rotor. The turbines require a source of heat to create the required steam. The heat can come from industrial processes (such as those in a refinery), a gas turbine (for combined-cycle operation), a fired boiler (heated by burning coal or biomass, or by a nuclear reactor), or from geothermal wells or concentrated solar heat collectors (such as the Ivanpah project in California, (US).
By power rating, this study addresses mechanical drive and combined-cycle power generation units ranging from 1-350 MW, but super-critical or ultra-super-critical units can have single-turbine output rating over 1 GW. These units are supplied by many of the same manufacturers as the smaller reference units and are included in the market size, but are not emphasized in the report.
The report addresses both condensing units and backpressure units. Condensing steam turbines are used in power generation applications, and operate a fairly constant pressure and speed of steam, regulated by varying the intensity of the heating application and by valves at the steam inlet.
Backpressure units are used for mechanical drive, and the main control valve is placed at the exhaust, regulating the pressure inside the turbine and the speed at which the rotor turns. Steam pressure ratings for both mechanical drive and non-super-critical power generation units typically fall in the range of 100 bar to 180 bar, although super-critical steam units for thermal power generation are rated for steam pressures of up to 250 bar.
As with gas turbines, this report focuses on the cost of the turbine itself, not including ancillary components, which would typically include boilers, heat recovery steam generators, and electrical generators.

## Slide 9
10
2 Methodological Notes
References to equipment types as proper nouns (where capitalization is used, e.g., “Gas Turbines Compressor”) are specific to the scope of equipment as outlined in the Scope section and further clarified by the Reference Product (see Reference Product Definitions and Scope). Continuing with the preceding example, “Gas Turbines Compressor” would be more specific than “centrifugal compressor”).
Demand is nominal (not real, inflation-adjusted), and is based on Sales excluding backlog that has not yet been recognized as revenue.
Prices are for new commitments. Average market prices typically lag the index based on the time it takes for pre-existing contracts to end or roll over. Price changes are nominal (not real, inflation- adjusted). Price changes are net of the cost of quality improvements, so actual market prices may exceed the amounts indicated.
Capacity includes base production capability plus plant openings and temporary capacity increases such as extra shifts, minus plant closings and temporary capacity reductions such as reductions of working hours or suspension of operations. Capacity estimates are unadjusted for possible efficiencies from process improvements. Capacity is adjusted for productivity improvements.
Capacity utilization means output as a percent of possible production, given no major investment. Capacity utilization rates are either self-reported or estimated. Orders above capacity to produce are considered backlog and do not result in capacity utilization rates above 100%. Overtime increases the capacity utilization rate and could make capacity utilization rates exceed 100%, whereas extra shifts count toward capacity and would not normally result in capacity utilization rates exceeding 100%.
Capacity Margin is the aggregate amount of available (unutilized) capacity based on utilization rates and total capacity. It is not adjusted for capacity that suppliers may have reserved for specific customers, so actual available capacity may be lower.
Order Lead Time is for Configure-to-Order (also called Assemble-to-Order), Make-to-Order, and where specified, Engineered-to-Order items, not for stocked/inventories items (for which lead time is very short). If categories consist only of stocked/inventoried items, lead time is not tracked. The basis is ex-works (from the time the order is placed until it is ready for shipping). Where there is a choice, Order Lead Time is based on oil and gas applications of higher-value items within each category (e.g., stainless steel rather than carbon steel, or with customizations such as ceramic coating).

## Slide 10
3 Vital Statistics
Table 1: Demand, Order Lead Time, Capacity Utilization, and Prices
Metric | Time Horizon | Gas Turbines |  | Steam Turbines | 
 | Q2 2013 |  | 6,649 |  | 5,535
 | Q2 2015 | ▲ | 6,936 | ▲ | 5,877
Demand ($M, per quarter) | Q2 2020 | ▲ | 8,361 | ▲ | 7,262
 | ‘13-‘15 | ▲ | 4.3% | ▲ | 6.2%
 | ‘13-‘20 | ▲ | 26% | ▲ | 31%
 | Q2 2013 |  | 51 |  | 63
 | Q2 2015 | ▲ | 52 | ▲ | 65
Order Lead Time (Weeks) | Q2 2020 | ▲ | 52 | ▲ | 68
 | ‘13-‘15 | ▲ | 2% | ▲ | 2.8%
 | ‘13-‘20 | ▲ | 2% | ▲ | 4.6%
 | Q2 2013 |  | 90% |  | 88%
 | Q2 2015 | ▲ | 91% | ▲ | 91%
Capacity Utilization (%) | Q2 2020 | ▲ | 91% | ▲ | 92%
 | ‘13-‘15 | ▲ | 0.8% | ▲ | 2.8%
 | ‘13-‘20 | ▲ | 1.0% | ▲ | 3.8%
 | Q2 2013 |  | 162 |  | 134
Prices (Index 2005 Q1 =100) | Q2 2015 | ▲ | 174 | ▲ | 143
 | Q2 2020 | ▲ | 197 | ▲ | 161
 | ‘13-‘15 | ▲ | 7.1% | ▲ | 6.8%
 | ‘13-‘20 | ▲ | 23% | ▲ | 22%

## Slide 11
4 Gas Turbines
4.1 Market Overview
Table 2: Key Indicators for Gas Turbines
(Total Change over Each Period)
Key Indicators | Q2 2013 – Q2 2015 |  | Q2 2013 – Q2 2020 | 
Demand Growth | ▲ | 4.3% | ▲ | 25.7%
Demand ($m) | ▲ | 6,649-6,936 | ▲ | 6,649-8,361
Capacity Utilization | ▲ | 0.6% | ▲ | 0.8%
Prices | ▲ | 6.8% | ▲ | 19.5%
4.1.1 Demand
Aggressive spending in Asia on power and natural gas projects will drive Gas Turbine demand up 1.7- 1.8% annually in 2013 and 2014 to 3-4% per year through 2020.
Capital spending on the part of power plants is the biggest driver of demand for Gas Turbines. This can be an extremely volatile source of demand, especially during periods of economic downturn.
Power utility capital spending fell 12% on a global basis in 2009 and grew just 3% in 2010, compared to annual growth of 11-25% from 2005 through 2008. The impact of these fluctuations in underlying demand on Gas Turbine sales is stabilized by the long lead time for the units themselves (typically a year or more), and the fact that payments stretch from order to delivery. For example, when power industry capital spending tanked in 2009, gas turbine demand fell by only 7%.
Similarly, when global utility spending grew by 20% from 2010 through 2012, gas turbine sales rose by only 12% over the same period.
The differential growth rate between natural gas prices and coal prices also impacts demand growth rates for both Gas Turbines and Steam Turbines. As natural gas becomes comparatively cheaper, gas turbines become a more attractive source of power compared to large-scale steam turbines (nearly 80% of which are driven by coal-fueled boilers). The inverse is also true. From 2005-2012, US coal prices more than doubled. In comparison, natural gas prices increased a net 8% (although they peaked at a 53% increase in 2008). This has helped boost demand for gas turbine-driven power generation compared to thermal power plants since 2009 (12% as mentioned above vs.
8.5% for Steam Turbines).
Gas Turbine sales rose slightly less than 0.5% in Q1, and will increase at a similar rate for the rest of 2013 – for annual growth of 1.7% this year. This year’s growth is driven in large part by the overall increase in utility capital spending - 4% globally.

## Slide 12
Asian demand is growing fastest, at 1.3% per quarter this year, driven by forecast growth of 8% in underlying power industry spending in the region. China is the clear leader in terms of turbine orders, but the demand growth is broad-based. Orders include:
In Korea, Kepco and Dongducheon Dream Power ordered a total of 10 M501J gas turbines from MHI in 2012, worth a cumulative $565m. Deliveries of the units will continue into 2014.
Power plants in China’s Zhejiang Province ordered a total of five GE 6FAs. Four of the units will be split between two combined-cycle plants; Datang International Power’s Jiangshan plant and Quzhou Puxing’s Quzhou Kecheng plant. Both plants will produce 230 MW of power, as well as heat for surrounding homes and businesses. The remaining unit went to Amber Energy’s 115 MW Anji combined-cycle plant.
Harbin Turbine Company has ordered four GT13E2 gas turbines from Alstom since 2012 Q3, for installation in China’s Shenzhen province, all of which have yet to be delivered.
Toyo Thai Power ordered two gas turbines from GE in 2012 Q4, collectively worth $27m for the turbines alone, LM6000-PC Sprint aero-derivative units for its Alhone power plant in Yangon City, Myanmar.
Asian natural gas production, processing, and liquefaction projects will also contribute to strong regional demand growth. Chevron ordered 11 gas turbines from GE for its Gorgon project on Barrow Island off the coast of Australia – five Frame-9 units for power generation and six Frame-7 turbines to drive the plant’s main refrigerant power trains. Equipment deliveries began in 2012, but will continue 2014. Petronas ordered six GE gas turbines for its FLNG project off the coast of Malaysia, four PGT25+G4 gas turbine generator systems and two PGT25+G4 gas turbine-driven compressor units. GE is scheduled to deliver the equipment to Malaysia in August 2013.
Demand will grow 0.3% per quarter in EMEA this year, supported by orders from the Middle East and Eastern Europe, as orders stagnate in Western Europe due to slow economic growth there. For example:
Siemens sold five 112 MW SGT6-2000E gas turbines to Saudi Electricity Company in May, for installation in Rafha, Qurayyat and Arar. The turbines alone are worth $114m.
EPC firm Metka S.A. ordered a GTE132 gas turbine from Alstom in May 2012, for installation in the Kingdom of Jordan, a 180 MW turbine worth $42m.
Dolphin Energy ordered three Trent 60 units for its subsea pipeline between Oman and UAE. Shipped in Q1 2013, the units were worth $12m each.
Slow economic growth in the US is curbing demand growth in the Americas this year, although orders from the US, Canada, and Mexico will help maintain 2013 demand at 2012 levels. The Americas region does not have fast-growing regions analogous to the Middle East and Eastern Europe as engines for growth, and with a larger market size ($7.8b in 2012 vs. $5.6b in EMEA), it

## Slide 13
5,000
4,000
3,000
needs more order volume in a given period to generate growth. Orders that will drive demand in the this year include:
Florida Power and Light ordered three SGT6-8000H gas turbines from Siemens in December 2012, for its Port Everglades Next Generation Clean Energy Center, a combined cycle plant scheduled to begin commercial operation in 2016. The $46.5m units will begin shipping from Siemens’ US plant in Charlotte in 2014, but progress payments will continue from this year through 2016.
Canadian power producer TransAlta Generation ordered two M501GAC gas turbines from MHI for its 800 MW Sundance 7 combined-cycle power plant. MHI will make the hot gas path components in Japan, but perform the bulk of the manufacturing, and all of the assembly, in Savannah (US). Full delivery of the $49m units is scheduled for late 2014.
The El Sauz power plant in Mexico ordered a GT24 gas turbine from Alstom in July 2012. The 230 MW unit sold for $39m and is scheduled for delivery later this year.
Also in Mexico, textile and chemical manufacturer CYDSA ordered a 61 MW Trent 60 WLE gas turbine from Rolls Royce in March, for approximately $15m.
Global demand will grow another 1.8% in 2014 as Western European spending remains slow, then accelerate to 3-4% annually beginning in 2015, as global utility spending growth stabilizes at 7% per year. Gas Turbine spending growth rates are not growing at the same rate as overall utility spending because utilities spend proportionately more on equipment that wears out faster, such as . substation and power distribution infrastructure, which need to be updated or replaced as often as every few years. In contrast, Gas Turbines operate for potentially decades.
Oil & gas spending accounts for just under 10% of Gas Turbine demand, and will continue to contribute to global gas turbine sales, with annual downstream capital spending growth of 8%, and upstream growth of 5% per year. As with utility spending, overall capital expenditures for oil & gas producers increases faster than gas turbine purchases because power requirements represent a relatively small portion of infrastructure requirements.
Figure 1: Demand for Gas Turbines
9,000
8,000
7,000
6,000
2,000
1,000
-
05 Q106 07 08 09 10 11 12 13 14 15 16 17 18 19 20
Sales in
Nominal Dollars ($M US)
Asia
EMEA
Americas

## Slide 14
Asian demand will continue to grow fastest, at 8-9% annually, on forecast economic growth in China of 6-8% per year. Slower growth (1-2% annually) in mature economies in North America and Western Europe, still held back by slow overall economies and public debt concerns, will keep Gas Turbine demand growth rates in the Americas and EMEA at 1-3% annually.
    Supply (Capacity)
GE, Siemens, MHI, Alstom, and Rolls Royce are adding enough capacity to stabilize utilization levels at 90% at current demand growth rates, primarily with targeted construction in major markets.
The top gas turbine suppliers are:
      GE (US)
      Siemens (Germany)
      Alstom (France)
      MHI (Japan)
      Rolls Royce (UK)
      Ansaldo (Italy)
      MAN (Germany)
      Doosan (Korea)
      BHEL (India)
      Kawasaki (Japan)
Capacity utilization rates are typically above 90% for gas turbine manufacturing operations because suppliers are willing to tolerate high backlogs and let extended lead times buffer them from overinvesting in production capacity during boom times. The Gas Turbine supply market is highly concentrated and the technological barriers to entry are high enough to discourage new competitors, leaving little risk that one supplier can win a great deal of business by investing in new capacity before the rest can respond.

## Slide 15
Figure 2: Capacity Margin – Gas Turbines
Industry capacity increased slightly (less than 0.5%) in 2013 Q1 as Siemens commissioned a new casing machining station and a test bed in Berlin, Germany. The incremental capacity addition closely matched demand growth, keeping overall capacity utilization at 90%. Siemens finished building an expansion in Berlin, Germany in 2012 Q4 featuring a new $16m drilling station for gas
turbine casing parts, which machines the components to final specifications. The station was built to increase process efficiency and automation, as well as to avoid backlog buildup for the components as demand grows. Siemens also added a $20m test bed at the plant.
Capacity Margin is $750m per quarter as of 2013 Q2 (compared to overall industry capacity of
$7,380m per quarter). At the industry level that is enough for nearly 100 of the smallest reference product, and 15 of the largest. To put this into perspective, an order for 10 of the largest reference unit would be an uncommonly large order, and orders from a single buyer rarely exceed $150m in total turbine value. Given the size of the overall industry, there is little risk of one or a few orders severely encroaching on capacity availability in the near future. However, the chances of a specific manufacturer being bottlenecked at a specific moment for a specific model of gas turbine are reasonably high.
90%
110%
$1,000
$900
$800
$700
$600
$500
$400
$300
$200
$100
$0
13 Q1 14
17
18 19
20
Utilization
Rate
70%
50%
Capacity Margin (Nominal
$M USD
per Quarter)
15 16
Capacity Margin
Utilization Rate

## Slide 16
GE, Siemens, Alstom, MHI, and Rolls Royce, are all planning to add capacity in 2013-2014, which will keep industry utilization rates stable (they currently stand at just over 90%). Some of the capacity additions are moves to target a particular market, and in the case of Siemens and Alstom, are balanced to some extent by concurrent reductions in regions where they have more capacity than they need.
Siemens opened a new gas turbine blade core production facility in Charlottesville, US, in 2013 Q2. The plant uses Tomo-Lithographic Molding (TOMO) technology to make cores that cool more evenly, increasing gas turbine efficiency. The plant does not increase Siemens’ overall gas turbine capacity, only adding capacity for more efficient blade cores.
Siemens will also open a new plant in 2013 Q4, a 700k square foot complex in Saudi Arabia. The $150m facility will employ 1k-1.5 workers at full production and make gas turbines and compressors, mainly to serve Middle Eastern orders.
To balance these capacity increases in other regions and to prepare for slow orders from Western Europe for the foreseeable future, Siemens is cutting capacity at its main gas turbine production plant in Berlin, Germany. It is reducing headcount by 1,100, and cutting unit capacity from 45 units annually to 35.
Alstom is adding capacity in Poland but cutting it in the US, to match production capabilities with demand growth patterns. It a opened a new turbine shaft welding shop in Elbląg, Poland, bringing rotor production standards in Elblag in line with Alstom’s other global plants. However, the firm cut headcount at its recently-built plant in Chattanooga, US, by 120 – a move that reduces capacity for both gas and steam turbines.
MHI will complete a new rotor production facility in Savannah, US in 2013 Q3. Rotors are the component with the second-longest lead time for MHI, after casings, and the new capacity will help bring down lead times for orders in Western Hemisphere.
100
Figure 3: Demand vs. Capacity – Gas Turbines
160
140
120
15
16
17
18
19
20
Capacity
Demand
Index
(2009
Q1=100) 80
60
40
13 Q1 14

## Slide 17
Kawasaki will add new capacity at its main facility in Akashi, Japan, in 2013 Q3. The new machines and headcount will give it the ability to manufacturer its new L30 (30 MW) model at a commercial scale.
GE invested $100m in a plant to make aero-derivative gas turbines in Shanghai, China. The plant is a JV facility with state-owned power company China Huadian Group, scheduled to open in 2013 Q4.
Rolls Royce is building a new packaging plant, with limited component machining capability, in Santa Cruz, Brazil. The unit will open in 2013 Q4.
GE is building another JV plant to make its 77 MW 6FA units in Russia, to match its cost base with price expectations in Russia and the CIS countries. The factory, which is under construction in Rybinsk, will have capacity for 14 gas turbines per year when it opens in 2014 Q2.
Siemens also made a move into the Russian power generation market, entering a joint venture with local supplier Power Machines to improve penetration in the CIS countries. Power Machines manufactures hydropower, thermal energy, nuclear power, and GTCC equipment and has a broad client base in former Soviet countries. Specifically, Power Machines will contribute to the joint venture with steam turbine and turbo-generator capabilities and Siemens will bring its gas turbine expertise. The joint venture will build an R&D facility in St. Petersburg, and manufacturing and service facilities near Moscow that are scheduled to open in 2014.
Table 3: Reported or Estimated Capacity Utilization Rates at Selected Gas Turbine Suppliers
Company | Country | Current Level | 12-Month Forecast
Siemens | Germany | 90% | 92%
Siemens | US | 85% | 85%
Alstom | US | 90% | 90%
Alstom | France | 85% | 88%
Ansaldo | Italy | 95% | 95%
MHI | Japan | 100% | 100%
MAN Turbo | Germany | 90% | 90%
Rolls Royce | China | 90% | 93%
Kawasaki | Japan | 88% | 90%
GE, Siemens, and Alstom, the largest gas turbine suppliers, set the trend for most aspects of the market, including technology, prices, and utilization rates. All three of these manufacturers are

## Slide 18
approximately 90% utilized presently. Alstom’s utilization rate was slightly lower, but its recent round of layoffs in the US has brought it into line with its biggest competitors. Smaller, but still major, suppliers Rolls Royce and MAN Turbo are also approximately 90% utilized.
MHI is 100% utilized for its larger range of power generation turbines (such as the M501J), but has some space available in the mechanical drive ranges (30-50 MW).
Kawasaki is the only major supplier that is less than 88% utilized, and it will have even more flexibility next quarter when the new machinery at its Akashi plant is commissioned, at a utilization rate of approximately 85%. The largest unit Kawasaki makes is 30 MW, however, so it only represents a potential capacity relief valve for smaller units.
Industry utilization rates will remain around 90% as suppliers work to maintain overall capacity
availability but avoid overbuilding. As a result, lead times will remain fairly constant on average, at
approximately 11-12 months for the 30 MW size range, 12-14 months for the 70 MW unit, and 14- 18 months for the 240 MW unit.
    New contracts
GE and Alstom won major contracts with long term service agreements, as well as most of the orders from China. Siemens and MHI won major utility orders based on their larger units’ high efficiency ratings.
GE and Alstom had the most success landing bundled equipment and long-term service contracts. GE in particular focuses on winning the service agreement to go with equipment sales. This gives it the opportunity to gather data on its units while in operation, and fold that expertise back into future design projects, as well as giving GE a stronger position on eventual bids to upgrade or replace the units.
      GE won a landmark order from Chevron’s Gorgon project. The size of the order and the wide range of the equipment and service provided are a major win for GE, and allowed Chevron to take full advantage of economies of scale and scope for the project. The order includes:
        Turbines:
          Five 130-MW Frame-9 gas turbines, custom-designed for power generation on Barrow Island’s gas treatment and liquefaction facilities
          Six Frame-7 gas turbines to drive the main refrigerant compressor trains
        Other equipment:
          Nine compressor trains – three refrigerant trains and six for Carbon Capture and Sequestration (CCS) (along with the motors to drive the CCS trains)
          20 subsea trees and wellhead systems
          Control systems for the entire spectrum of equipment
          Five pipeline termination systems, five manifolds, 34 pipeline end terminations and several other structures, including pig launchers/
receivers and umbilical distribution assemblies, 45 spools and 18 multi- bore well jumpers.

## Slide 19
20
o Service Agreement: a 22-year service agreement worth more than $600m
Scheduled maintenance
Permanent on-site engineers
Monitoring and diagnostics of the installed equipment, coupled with engineering analytics
Production continuity guarantees
Inventory management
Initial spare components
GE signed a $620m LTSA with the Queensland Curtis LNG project, covering planned and unplanned maintenance of the GE equipment being installed at the QCLNG plant, including 15 PGT25+G4 aeroderivative gas turbines, 28 centrifugal compressors, gearboxes, generators and all auxiliaries. The agreement also includes monitoring and diagnostic services, as well as reliability guarantees on the equipment.
GE will supply gas and steam turbines, generators and a plant-wide control system for the Phase 2 expansion project that will position Emirates Aluminum (EMAL) as one of the largest single-site aluminum producers in the world. In addition, GE will provide its latest technology upgrades for its gas turbines currently operating Phase I of the EMAL complex. The technology upgrades will include GE’s latest dry low nox (DLN) 2.6+ combustion technology, which is expected to lower nitrogen oxide (NOx) emissions, as well as extend the lifespan of gas turbines parts by up to three times.
GE will provide a Frame 9F 5-series gas turbine and generator to Abengoa, the engineering, procurement and construction contractor for the Stalowa Wola project, a new 450-megawatt, combined-cycle power plant in the city of Stalowa Wola that will be the largest gas-fired project in Poland, with a Gas Turbine worth about $54.6m. GE also has signed a separate contract with Abengoa to provide maintenance services for the plant for 12 years.
Alstom signed a $322m LTSA with General Electricity Company of Libya (GECOL) covering repairs and spare parts for 11 gas turbines at five different power plants. The 11 GT13 turbines were originally provided by Alstom.
Alstom signed two maintenance contracts worth $175m in the Middle East and Africa in Q4 2012. A contract with the Azito power plant in the Ivory Coast covers delivery of spare parts, reconditioning services, and inspection supervision for the gas turbines and generators for 15 years. The contract for the Samra III power plant in Jordan spans a 10 year period and includes the delivery of new and reconditioned parts as well as supervision manpower for the execution of major inspections on all three GT13E2 units installed at the plant.
GE and Alstom, which have invested heavily in Chinese manufacturing facilities, won most of the major contract awards in China, the fastest-growing regional market. Rolls Royce is now making a stronger effort to expand its presence in China, adding 20 staff at its Hong Kong Office to plan a
build-out and partnership strategy to gain market share. Examples of GE and Alstom’s recent contract wins in China include:

## Slide 20
GE sold five 6FA units to power plants in China’s Zhejiang Province. The units were delivered to the contractors building the plants in Q4 2012, although the purchase agreement was negotiated by the provincial government to leverage higher unit volume. It was effectively the only lever available, as domestic firms are providing the steam turbines and balance of plant. Four of the units will be split between two combined-cycle plants; Datang International Power’s Jiangshan plant and Quzhou Puxing’s Quzhou Kecheng plant. Both plants will produce 230 MW of power, as well as heat for surrounding homes and businesses. The remaining unit went to Amber Energy’s 115 MW Anji combined-cycle plant.
Alstom has sold a total of five GT13E2 gas turbines to Harbin Turbine Company (HTC) since Q3 2012. The first unit, ordered by HTC for installation at a combined cycle plant owned by Shenzhen Nantian Electric Power Co., Ltd in Shenzhen, was a pilot project for the two companies, and successful execution of the order facilitated another two orders. The price for the unit, $30m, was roughly consistent a discount of approximately 20% vs. global pricing levels, accounting for a difference in the price Chinese buyers are willing to pay. The following two orders, for two GT13E2 gas turbines each, included an additional discount of approximately 10% to account for economies of scale – for a unit price of
$27.5m each. The orders included only the gas turbines, however, as HTC can source local equipment such as alternators and mechanical auxiliaries in China at a lower cost. In the case of steam turbines, Harbin will supply the units itself.
Siemens and MHI won multiple, high-profile utility orders for their largest, most efficient units. Utility customers are typically most concerned with efficiency, and MHI’s M501J and M701J units have the highest simple-cycle efficiency rating of any turbine currently on the market at 41%, followed closely by Siemens 8000h series at 40%.
Florida Power and Light ordered three SGT6-8000H gas turbines from Siemens in December 2012, for its Port Everglades Next Generation Clean Energy Center, a combined cycle plant scheduled to begin commercial operation in 2016. The gas turbines’ efficiency rating drove FPL’s decision to order these units, which operate at over 60% efficiency in combined cycle. FPL has now ordered seven of these units from Siemens, one is already operating at its Cape Canaveral power plant, and three more are currently being installed at Riviera Beach. Among the drivers of the decision to order the same units is the reduction in maintenance training and spares pools. By ordering similarly- configured units, FPL was able to secure a discount of nearly 10% off the bare turbine price of $51.6m, for a unit price on this order of $46.5m
MHI booked four orders for a total of 10 M501J gas turbines (and five steam turbines, as well as HRSGs and electrical generators) from Korean power producers. Meiya power ordered its two units independently, and as a result paid a higher unit price ($54m vs 42m for the other eight units). KEPCO handled the negotiations for the remaining eight units,

## Slide 21
negotiating a 15% combined discount for volume, and another 10% in exchange for bundling the gas turbines, steam turbines, and HRSGs.
Saudi Electricity Company ordered five SGT6-2000E gas turbines from Siemens in May 2013, along with associated auxiliaries, packaging, and a 380 kV substation to tie the power into the grid. The total contract is worth approximately $270m, of which the gas turbines themselves make up about $114m. This includes discounts of approximately 10% between economies of scale for the five turbines and economies of scope for the associated equipment and substation.

## Slide 22
Table 4: Summary of New Contracts and Estimated Values for Gas Turbines
Buyer | Country of Installation | Supplier | Product | Estimated Value ($m) | Estimated Cost/Unit ($m) | Estimated Cost per kW
Chevron | Australia | GE | Five Frame-9 units and six 7EAs | $178 | $16.2 | $150
Korea Electric Power | Korea | MHI | Four M501Js | $169 | $42.3 | $129
Dongducheon Dream Power | Korea | MHI | Four M501Js | $169 | $42.3 | $129
NextEra Energy | USA | Siemens | Three STG6- 8000Hs | $139 | $46.5 | $170
Virginia Electric | USA | MHI | Three M501GACs | $138 | $46.0 | $169
EMAL | UAE | GE | Three Frame 9Fs | $129 | $43.0 | $165
Saudi Electricity Company (SEC) | Saudi Arabia | Siemens | Five SGT6-2000Es | $114 | $22.8 | $204
Meiya Power | Korea | MHI | Two M501Js | $107 | $53.6 | $164
ESB | UK | Alstom | Two GT26s | $105 | $52.6 | $164
TransAlta | Canada | MHI | Two M501GACs | $97 | $48.5 | $178
Cheniere Energy | USA | GE | 12 PGT25+G4 aeroderivatives | $89 | $7.4 | $225
Isolux Ingenieria | Bangladesh | GE | Two Frame 9F 3- series | $89 | $44.5 | $131
Harbin Electric Corporation | China | GE | Five Frame 6FAs | $64 | $12.8 | $165
Harbin Turbine Company (HTC) | China | Alstom | Two GT13E2s | $55 | $27.6 | $150

## Slide 23
Buyer | Country of Installation | Supplier | Product | Estimate d Value ($m) | Estimated Cost/Unit ($m) | Estimated Cost per kW
HTC | China | Alstom | Two GT13E2s | $55 | $27.6 | $150
RheinEnergie | Germany | Alstom | One GT26 | $54 | $54.0 | $169
Abengoa | Poland | GE | One Frame 9F | $46 | $46.4 | $156
Baotou Steel | China | MHI | Two M701DAs | $46 | $22.9 | $159
JSC Mosenergo | Russia | Alstom | One GT26 | $44 | $43.8 | $137
Petronas | Malaysia | GE | Six LM aero- derivatives | $43 | $7.2 | $218
Metka S.A. | Jordan | Alstom | One GT13E2 | $42 | $41.9 | $227
ACS Group | Mexico | Alstom | One GT24 | $39 | $39.1 | $170
Dominion | USA | GE | Two Frame 7EAs | $38 | $18.8 | $212
Dolphin Energy | UAE | RR | Three Trent 60s | $36 | $11.8 | $230
HTC | China | Alstom | One GT13E2 | $30 | $30.5 | $165
Lukoil | Russia | RR | Two Trent 60s | $30 | $14.8 | $231
Xstrata | Australia | Siemens | Two SGT-800s | $24 | $12.1 | $258
Asia Trans Gas | Uzbekistan | RR | Three RB211s | $23 | $7.7 | $228
Medco Power | Indonesia | GE | Two Frame 6Bs | $23 | $11.3 | $268
Thai Power | Myanmar | GE | Two LM6000-PCs | $21 | $10.7 | $213
Statoil | Netherlands | GE | One LM6000, one LM2500 | $21 | $10.6 | $237
Shell | Phillipines | RR | Two RB211s | $16 | $8.1 | $298
Edo Cement | Nigeria | Siemens | Three SGT-500s | $15 | $5.0 | $264
CYDSA | Mexico | RR | One Trent 60 | $14 | $13.6 | $222

## Slide 24
4.2 Analysis
4.2.1 Costs
Metals and metal components, labor, and energy costs make up most of the cost to manufacture gas turbines. Labor costs in Asia will rise fastest, but all of these factors will rise gradually through 2020.
Metals and metal components are the largest cost component for Gas Turbines, at 47% of the total. The metals used to make gas turbines comprise a wide range, from carbon steel and aluminum for much of the casing to titanium for the internal compressor components, nickel, and nickel-cobalt alloys for the combustion chambers and hot gas path. Many of these components are outsourced, such as blades, because of the expertise required to make and test them. Casting blades is complex, with internal heat dispersion characteristics that cannot be recreated without precise internal scans (such as a CT scan). For example, PSM (Alstom) tried to copy the 7FA blade for a year before it produced a viable blade.
Labor and benefits constitute another 29%. Professional labor, including engineering and management salaries, equates to 12% of the overall cost, including engineering activities such as initial compressor model design, materials research, constant component upgrades to keep older models technologically up-to-date, and customization work for many units. Production labor for gas turbines (10% of the total) is more expensive than for many types of equipment due to the specialized materials and machinery used to make them, which limits the number of machine operators, welders, and technicians qualified to work on the units.
Energy account for most of the rest of the manufacturing cost. Making gas turbines is an energy- intensive process, including multiple casting processes for casings, rotor sections, and blades.
Heating, forging, welding, and machining many of these components to finish them also drains energy, especially for nickel superalloys that are difficult and time-consuming to work.
Costs for steel will grow slowly and gradually through 2020, increasing at annual rates of 1.5-2%, driving costs for most grades and steel-based alloys up by similar amounts. Alloying material costs, such as nickel and cobalt, are historically more volatile, but long-term buying strategies for most manufacturers help to smooth out these costs except during the widest of swings. For example, Siemens avoided a spike in metal prices in early 2011 by adopting a dual stockpiling and fixed-price strategy. It negotiates raw price commitments for six months at a time. In case there happens to be a price increase, stockpiling serves as a cushion for cost control in the coming six month period.
Energy costs will rise fastest through 2020, at average rates of 2-2.5% per quarter, driven by aggressive fuel and electricity demand growth in China and India (electricity demand is up up 9% and 7% year-on-year in May in China and India, respectively).
Global labor costs will increase gradually at approximately 1.5% annually. Over the past year labor costs for gas turbines have been depressed to some extent by sluggish hiring markets in the US and Western Europe, and by recent layoffs at Siemens and Alstom. Moving forward, Asian labor

## Slide 25
costs will drive regional manufacturing costs up at a disproportionately high rate. In major Asian manufacturing areas (urban sectors with access to transportation infrastructure), costs of living are rising rapidly. Combined with the specialized training required to make gas turbines, this is driving Asian labor costs up more than twice as fast as in other regions. In Q1, professional labor costs rose 2% in Asia, compared to less than 0.5% in EMEA and the Americas. Asian production labor costs rose about 1%. This disparity in labor cost growth drove Asian costs up almost 1% for the quarter, vs. 0.25% growth in the other two regions. Asian labor costs are becoming increasingly relevant for gas turbine manufacturer such as GE and Alstom, which have expanded production capacity there recently.
The use of new technology substantially impacts the cost of a gas turbine. For example, Siemens helped develop and then licensed Mikro Systems’ TOMO composite blade casting technology, which cuts blade manufacturing lead time by 67% and reduces combined design and production costs by 50%, as well as raising turbine efficiency via increased temperature tolerance of the blade. While the technology development costs are still being amortized, this process will reduce Siemens’ manufacturing costs going forward, now that it has opened a full-scale manufacturing plant using the technology in the US.
Figure 4: Cost Structure for Gas Turbines
Note: Prices are ex-works.
Global cost levels were stable in Q1, as a slight decline in metals costs due to weaker than expected demand balanced out an increase in Asian labor costs. Global cost levels will rise at annual rates of approximately 1.5% in from 2013 -2015, after which point cost growth will accelerate slightly to 2% annually due to improving economic conditions and rising inflation in the US and
160 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
140 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
120 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Manufacturing 100 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cost |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Breakdown | 80 |  |  |  |  |  |  |  |  |  |  |  |  | 
(2006 Q1=100) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
60 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
40 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
20 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
06Q1 07 |  | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Energy Metals |  | Other Materials Production Labor |  |  |  |  | Motors Professional Labor |  |  |  |  | Benefits Machinery and Parts |  | 
Western Europe. This will compound to cost growth of 15% from 2013 Q2 through 2020 Q2.

## Slide 26
27
    Profit Margins
Supplier operating margins average 10%. They are higher in general for aero-derivative turbine manufacturers GE and Rolls Royce, and lower for Japanese suppliers MHI and Kawasaki.
Operating margins at the relevant business units of the major manufacturers average 10%, although the range is broad (6-20%).
      GE: Power and Water division (US), 19%
      Siemens: Fossil Power Generation division (Germany), 6%
      Alstom: Power division (France), 5.9%
      MHI: Power Systems division (Japan), 4%
      Rolls Royce: Power Generation division (UK), 11.5%
      MAN: Turbomachinery division (Germany), 6%
      Doosan: Energy division (Korea), 8.4%
      BHEL: Power division (India), 14.8%
      Kawasaki: Gas Turbines division (Japan), 4.4%
The industry as a whole profits when times are good. Average operating profit margins doubled from 8% to 16% from 2003 through 2008, then reverted to 8% in 2009-2010. They have since risen slightly, but have been held down by weak demand growth in the US and Europe.
GE and Rolls Royce have the highest operating margins of the major global suppliers, primarily because they supply aero-derivative gas turbines (in addition to industrial units). Margins on these units are frequently twice as high as those for industrial machines, according to GE. Buyers pay substantially more for aero-derivative units because they are more efficient and have a smaller footprint, which reduces related costs in space-constrained applications such as offshore platforms. This results in both higher prices and higher margins for manufacturers.
As with other equipment markets, Japanese manufacturers earn lower operating margins than most of their competitors, due primarily to their higher cost base in Japan vs. the need to price competitively to win orders. MHI’s Power Systems business unit and Kawasaki’s Gas Turbines division made operating margins of approximately 4% in 2012. Excluding these figures from the global average, industry operating margin rose to 11%. In contrast, BHEL, one of the few manufacturers based in a low-cost region with trackable margins, made operating margin of almost 15% in its Power division last year, reflecting both a somewhat lower cost base and restricted competition in India due to many buyers’ policy of favoring domestically-supplied equipment where possible.
Going forward, stronger demand growth beginning in 2015 and persistently high industry capacity
utilization will allow manufacturers to regain margin levels that have declined during the economic

## Slide 27
slowdown. While cost levels will rise approximately 15%, prices will rise 23%, indicating as much as
an eight percentage point increase in overall supplier margin levels by 2020 Q2.
  Prices
Prices are growing steadily, which allows both buyers and suppliers to plan for capital projects with some degree of certainty.
Average prices for the reference units covered in this study are $24.5m. The range is broad however, and the reference units and prices at benchmark levels (without bundling or volume discounts) in mature markets are listed below. These reference prices are for the bare turbine, not a turbine generator or drive package, to facilitate more accurate comparison and to eliminate the impact of regional packaging differences.
    Reference unit 1:
      30 MW gas turbine used for mechanical drive on an Enhanced Oil Recovery (EOR) pump unit in field operation.
      Price: $8.8m
    Reference unit 2:
      70 MW gas turbine used for mechanical drive on a refinery pump or compressor, or small-scale simple-cycle power generation.
      Price: $18m
    Reference unit 3:
      240 MW gas turbine used for combined-cycle power generation.
      Price: $47m
Prices increased slightly in 2013 Q1, less than half a percent on average, as some manufacturers negotiated higher prices for new units. Siemens in particular is gaining ground pushing through price increases now that its new blade manufacturing center (which increases turbine efficiency through more effective blade cooling) is operational. Overall costs remained stable, however, and the price increase is attributable to rising capacity utilization levels and efficiency premiums.
Global prices will rise a total of 2.5% in 2013 due to the same factors, although costs will only increase 1.5% this year. GE, Alstom, MHI, and Rolls Royce are also adding machinery and manufacturing units at existing plants to update their technology base and increase unit efficiency, which will justify at least some of this higher profit margin.
Demand-based pricing and technology surcharges will continue to drive prices, rather than costs, as Gas Turbine prices will rise a total of 23% by 2020 Q2. While new technology will continue to get more expensive, the reverse is typically true for technology that is replaced by newer models or becomes obsolete. Price cuts for older technology are highly situational and dependent both on the buyer and the technology, but can contribute to substantial cost reductions for buyers if they are willing to install older technologies (which is prevalent in markets such as the Middle East where

## Slide 28
natural gas is cheap or free and efficiency is less of a concern). This is one of the ways that suppliers meet price expectations in different global regions.
Figure 5: Overall Price Forecast for Gas Turbines
35
30
25
Cost 20
per
Unit ($m) 15
10
5
-
2004 2006 2008 2010 2012 2014 2016 2018 2020
Min Global Average Max
“Country pricing” plays a strong role in the final price paid by buyers for a gas turbine. According to Siemens, the full package price of a gas turbine generator it sold in Turkey recently was $13m, compared to $19m for the same model sold in Germany (a 32% difference). This price variation was largely due to the German customer’s specification of multiple deluxe options (e.g. inlet air fogging, stainless steel cooling water tankage and supports, and a four-week string test of the package compared to the standard 72 hours). However, the price in Turkey was still 15% lower than the standard unit price in Germany after backing out differences in options and auxiliaries.
As mentioned above, suppliers typically offset the impact of regional price differences by substituting older technology, which lowers their manufacturing costs, which in turn preserves their margins. This value engineering typically focuses on combustion, sensor, and control systems. For example, eliminating the dry low nox combustion system typically included in most current models, a supplier can reduce the manufacturing cost of the unit by 5-6% in one stroke, allowing it to offer a more substantial “country-based” discount. They also attempt to use more local components where available (e.g. the strategy of building local capacity to supply major domestic markets in China and Eastern Europe adopted by GE, Siemens, MHI, and Alstom).
The following regional comparisons are based on a combination of cost factors that drive buyers’ price expectations, supplier feedback on the prices buyers are willing to pay, and indicative contract data.

## Slide 29
30
Table 5: Regional Price Variations over Time for Gas Turbines
Region/Country | Today | 2014 | 2015 | 2020
North America | 1.00 | 1.00 | 0.99 | 1.08
Latin America* | 0.90 | 0.94 | 0.97 | 1.14
Europe | 1.05 | 1.07 | 1.07 | 1.15
Africa* | 0.85 | 0.87 | 0.86 | 0.95
India | 0.82 | 0.84 | 0.85 | 0.99
Russia | 0.85 | 0.89 | 0.90 | 1.06
China | 0.80 | 0.81 | 0.80 | 0.88
Japan | 1.10 | 1.12 | 1.12 | 1.16
Other Asia* | 0.90 | 0.91 | 0.92 | 1.00
Notes:
“*” means supplied by foreign manufacturers only
Chinese buyers expect the lowest costs. Local manufacturers such as Shanghai Electric can license technology from global manufacturers and make them for the domestic market at lower costs, so global manufacturers must meet those cost expectations to make a sale in the country. Package costs are typically 30% below “list price” levels based on mature market prices, and the bare turbine price is typically 20% lower. For example:
The five 6FA units that GE sold to power generators in China’s Zhejiang Province went for a discount of 20% (additive to other discounts for order volume).
When Alstom sold a GT13E2 to Shenzhen Nantian Electric Power in late 2012, the price for the unit, $30m, was consistent a discount of approximately 20% vs. global pricing levels.
Baotou Iron & Steel ordered two combined cycle plants in 2012 Q3 to generate power from blast furnace gas created by its steelworks in Baotou City (Mongolia). MHI will supply the first of the units (using its M701S (DA) gas turbine), delivering the equipment in 2014 Q2. Chinese Dongfang Turbine will manufacture the equipment for the second unit, under license from MHI, scheduled for delivery in 2014 Q3. The total value of the gas turbines is approximately $46m, nearly 20-25% below MHI’s normal selling price. This is, in part, achieved by migrating production of the second unit to Dongfang’s Chinese facilities.
India is also a relatively less expensive market. Alstom sold a combined cycle plant to GVK Industries in India in 2013, at overall contract values 15-20% lower than similar contracts in Europe.
Russian price levels are typically about 15% below global price levels. This is based on robust competition from local manufacturers compared to most regions – in the form Russian suppliers ZM Turbines and Perm Motors and Ukrainian Motor Sich – as well as a strong migration of global suppliers GE, Siemens, and Alstom into Eastern European Manufacturing capacity.

## Slide 30
Data on Africa is scarce, due in large part to the comparatively small number of units sold there. However, Nigerian Edo Cement ordered three SGT-500s from Siemens in Q2 2013, each rated for 19 MW in electrical output. The turbines alone sold for $5m each, for a total of $15m, approximately 20% below Siemens typical asking price for these units. Regional pricing accounted for most of the difference, although Siemens gave Edo about a 5% price cut for order volume.
Latin American price levels are typically 10% below those in North America and Europe. For example:
Alstom sold one GT24 to the El Sauz combined cycle power plant in Mexico in July 2012, replacing an old gas turbine (installed in 1981). The turbine sold for 11% less than 2012 benchmark prices - $51.7m for the package and $39m for the turbine itself. Given the lack of economies of scope and scale (for just the one turbine) the discount is evidence of “country pricing.”
Rolls Royce sold a Trent 60 WLE gas turbine to Mexican textile and chemical manufacturer CYDSA to power multiple plants (and sell electricity to the grid), in Vera Cruz. Scheduled for delivery later this year, the turbine sold at a discount of 10% to account for price differences in the Mexican environment.
4.3.1 Price Differences by Technology, Model, and Feature
Increasing unit power rating increases absolute cost but decreases the cost per kW. Buyers pay a premium for efficiency that decreases with unit size.
At the most basic level, the price of a gas turbine is determined by its size, most commonly
denominated in MW of electrical output, or horsepower for mechanical drive units. For ease of
comparison, all units are described by MW rating (which equates to horsepower rating times 0.745). Cost per incremental MW decreases with unit size, as described in the tables below for the reference units covered in this study.

## Slide 31
Table 6: Incremental Cost per Parameter or Feature for a 25-35 MW Gas Turbine
(based on the reference unit specified above)
Parameter or Feature | Unit of Measure | Indicative Cost Impact | Notes / Comments
Output Power Rating | MW (30 MW as reference point) | Selecting a unit rated for 25 MW reduces cost by $1.2m. Increasing to 35 MW costs $1.2m more. | Costs accelerate rapidly with MW rating in this power range, and increases are virtually linear.
Cost Premium per Incremental 1% of Efficiency | % efficiency (36% as reference at 30 MW) | A unit that is 1% more efficient (37%) costs approximately $6-8 more per kW. | Cost increases per incremental unit of efficiency decline dramatically as output power rises
Packaging, Installation, & Commissioning | $ per unit ($6.5m as reference at 30 MW) | Costs for packaging, installation, and commissioning amount to $5.6m for a 25 MW unit, and $7.4m for a 35 MW turbine. | Packaging, installation, and commissioning adds 73% to the cost of the bare turbine in this size range.
Note: Changing one parameter usually involves changing others, and the cost impact may not be additive or linear.
Buyers pay a premium for higher efficiency. This is due in large part to the suppliers’ need to amortize their investments in new technology to increase turbine efficiency. Siemens’ recent investment in a plant to make blade cores with new TOMO heat distribution is just one example. It is also derived from the incremental value for buyers of getting more power out of a unit with the same footprint. This is especially valuable for applications such as offshore platforms, where space is costly.

## Slide 32
Table 7: Incremental Cost per Parameter or Feature for a 50-85 MW Gas Turbine
(based on the reference unit specified above)
Parameter or Feature | Unit of Measure | Indicative Cost Impact | Notes / Comments
Output Power Rating | MW (70 MW as reference point) | Down-selecting a 50 MW reduces cost by $4m. Upgrading to 85 MW costs an additional $2.8m | Cost growth slows as power rating increases due to economies of scale for the manufacturer.
Cost Premium per Incremental 1% of Efficiency | % efficiency (36% as reference at 70 MW) | A unit that is 1% more efficient (37%) costs approximately $4-6 more per kW. | Correlation of cost per kW with efficiency increases is weak for power generation turbines due to the proliferation of options such as quick-start, low emissions, etc., but the efficiency premium declines as unit power rating increases.
Packaging, Installation, & Commissioning | $ per unit ($10m as reference at 70 MW) | Costs for packaging, installation, and commissioning amount to $7.7m for a 50 MW unit, and $11.5m for an 85 MW turbine. | Packaging, installation, and commissioning adds 56% to the cost of the bare turbine in this size range.

## Slide 33
Table 8: Incremental Cost per Parameter or Feature for a 220-270 MW Gas Turbine
(based on the reference unit specified above)
Parameter or Feature | Unit of Measure | Indicative Cost Impact | Notes / Comments
Output Power Rating | MW (240 MW as reference point) | Selecting a unit rated for 200 MW reduces cost by $6.3m. Increasing to 270 MW costs $5.2m more. | Cost growth slows as power rating increases due to economies of scale for the manufacturer.
Cost Premium per Incremental 1% of Efficiency | % efficiency (38.5% as reference at 240 MW) | A unit that is 1% more efficient (39.5%) costs approximately $2-3 more per kW. | Correlation of cost per kW with efficiency increases is weak for power generation turbines due to the proliferation of options such as quick-start, low emissions, etc., but the efficiency premium declines as unit power rating increases.
Packaging, Installation, & Commissioning | $ per unit ($28m as reference at 240 MW) | Costs for packaging, installation, and commissioning amount to $24.3m for a 200 MW unit, and $31.2m for a 270 MW turbine. | Packaging, installation, and commissioning adds 60% to the cost of the bare turbine in this size range.

## Slide 34
Figure 6: Gas Turbine Cost vs. Power Output
$-
$30
$20
$10
$60
$50
$40
0
300
Unit Cost ($m)
100 200
Unit Output (MW)
Pump Drive
Small Scale Powergen or Refinery Turbo Drive
Combined-Cycle Power Generation
$5
$-
0
10
20
50
60
70
The correlation between efficiency and a higher price point is strong for mechanical drive units, but less evident for power generation turbines due to a proliferation of options for units sold in the market. These options include quick-start capability and low emissions combustion systems.
Figure 7: Gas Turbine Cost Premium per Incremental 1% of Efficiency (Mechanical Drive)
$25
$20
$15
Incremental $
per kW for a 1% $10
Increase in Efficiency
30 40
Unit MW Rating

## Slide 35
The correlation between incremental efficiency and higher cost per kW is weaker for power generation units than for mechanical drive turbines, based on commercially available models. However, the cost premium exists in both cases, indicating that buyers are willing to pay more for a smaller unit footprint in the case of the smaller units, and the increase in output for the larger power generation turbines.
$10
$8
$6
$4
$2
$-
Figure 8: Gas Turbine Cost Premium per Incremental 1% of Efficiency (Combined Cycle)
$18
$16
$14
$12
0
50
150
200
Incremental $
per kW for a 1% Increase in Efficiency
100
Unit MW Rating

## Slide 36
Cost per kW of generating capacity falls rapidly in the smaller turbine ranges, but the incremental cost reduction flattens in for the larger power generation units. This flattening occurs due to higher engineering costs to increase efficiency, the primary concern for utility buyers, and higher materials costs to cope with higher firing temperatures.
Figure 9: Gas Turbine Cost per kW of Generating Capacity
Turbine packaging, installation and commissioning adds significant costs for all three reference unit sizes. For the 30 MW range (for mechanical drive), it increases cost by 73%. For mechanical drive applications, packaging includes a heavy-duty gearbox, inlet air filtration system including ducting, silencers, exhaust stack; mechanical auxiliaries including output drive shaft coupling, startup and lube-oil systems, temperature and vibration monitoring systems, turbine controls, and fire suppression system. Power generation auxiliaries for the 70 and 240 MW units include: an electrical generator, intake and exhaust system, and mechanical and electrical auxiliaries. For all of the model variations, installation and commissioning includes onsite engineers to oversee turbine installation and the supply and connection of piping, cabling, electrical wiring, as well as onsite system testing.
The above figures are highly variable depending on the options chosen by the supplier, and can vary further depending on the choice of packager. The OEM will typically use purpose-built components for its own models, and charges a premium for onsite engineers. Third party packagers and installation engineers are typically cheaper, but do not offer the same performance guarantees or have the same level of expertise with the OEM’s equipment.
Manufacturers achieve economies of scale for all three reference unit ranges, although they are more noticeable for the larger units. Discounts for economies of scale can reach
$100
$-
$500
$400
$600
0
300
$ per $300
kW
100 200
Unit MW Rating
Pump Drive - Bare
Small Scale Powergen or Refinery Turbo Drive - Bare
Combined-Cycle Power Generation - Bare
$200
Pump Drive - Installed
Small Scale Powergen or Refinery Turbo Drive - Installed
Combined-Cycle Power Generation - Installed

## Slide 37
Economies of scale and scope are the biggest sources of cost savings for most buyers with large
project requirements. At a reference order quantity of 10 units buyers can get 10-15% off of list
price for ordering more units, according to manufacturers. Beyond ten units, manufacturers typically do not offer substantial additional price discounts for unit ordered. For example, Saudi Electricity Company received a discount of 13-14% for its order for 30 gas turbines for it’s a power plant near Riyadh in September of 2009. Engineering costs can be spread across multiple units and the supplier avoids machinery configuration changes. Bundling gas turbines with other equipment is also common, especially for mechanical drive units which are often sold in a package with the machinery they will drive. Savings in this category for major projects that include multiple drivers and process units (pumps or compressors) can amount to 10% for 10 units.
Competitive bidding can reduce initial purchase cost by about 5%, based on other contract negotiations. This percentage is not larger because of the limited number of suppliers, regardless of the unit, and because suppliers tend to know each other’s prices and price close to one another. As a result, some buyers forego bidding by single-sourcing or specifying a unit that only one or two manufacturers can manufacturer without significant design work.
Value engineering typically can reduce unit cost, potentially by as much as 10-20%, but it almost always comes at the cost of reduced turbine reliability or efficiency. As described in the Prices section, the manufacturer can substitute less expensive and older technologies to reduce the cost of the unit, but this results in a machine built to lower than the current industry standards. As a
$30
$25
$20
$15
$10
$5
$-
10% for the 30 MW range of turbine
15% for the 70 MW units
15% for the 240 MW units
Figure 10: Gas Turbines Economies of Scale
$50
$45
$40
$35
Unit
Cost
$m
0 2 4 6 8 10
Units Ordered
4.3.2 Should-Cost Analysis
30 MW
70 MW
240 MW

## Slide 38
4.4 Price Negotiation Strategies
Consider using long-term framework agreements with cost indexing clauses to avoid impending price increases from manufacturers that are not related to costs. Accelerating demand growth and tight capacity utilization will allow manufacturers to raise price by as much as 8% more than costs by 2020. Even if signing a framework agreement reduces the savings from competitive bidding by half, for net savings of 5.5%, this would amount to savings of nearly $1m per unit on the 70 MW reference unit, in isolation from other variables.
Evaluate each project for footprint requirements vs. efficiency. Buying a smaller, more efficient unit costs more per kW of generating capacity, and it may be more cost-effective to buy a less efficient unit if space is cheap.
Obtain economies of scope for gas turbines by tendering the equipment as a package (turbine, auxiliaries, and the machinery driven by the turbine). Even if the supplier is only selected for the bare turbine, some of the negotiated discount can stick to the turbines. GE is especially likely to
1.2
0.0
3.1
2.5
0.0
17.8
5.0
-
10.0
20.0
25.0
consequence, buyers in the oil & gas market usually do not look for cost savings through value engineering. Value engineering requested by buyers in the oil & gas industry typically increases the cost of the unit, if anything, because these buyers are more interested in improving performance.
For example, Statoil paid almost 10% more in custom engineering fees for two GE gas turbines for its Aasta Hansteen offshore development because it need reduced footprint. As with any rotating equipment, the focus of cost management for Gas Turbines should be on lifecycle cost, which first and foremost requires specifying the optimal equipment for the job. The potential savings from lifecycle cost management typically exceed the savings on the initial purchase cost.
Figure 11: Should-Cost for Gas Turbines
30.0
Base Cost
Competitive Bidding
Value Engineering
Economies of Scale
Economies of Scope
Supply Chain Integration
Should Cost
$m 15.0
24.6

## Slide 39
40
offer bundling discounts, due in large part to its extensive range of equipment and in-house packaging capabilities.
4. Secure discounts for economies of scale by ordering as many units as possible together. Maximize these discounts by collaborating with the supplier during the design and specification stage to find specification parameters that will allow the manufacturer to standardize components and engineering processes.

## Slide 40
5 Steam Turbines
5.1 Market Overview
Table 9: Key Indicators for Steam Turbines
(Total Change over Each Period)
Key Indicators | Q2 2013 – Q2 2015 |  | Q2 2013 – Q2 2020 | 
Demand Growth | ▲ | 6.2% | ▲ | 31.2%
Demand ($m) | ▲ | 5,535-5,877 | ▲ | 5,535-7,262
Capacity Utilization | ▲ | 2.8% | ▲ | 4.0%
Prices | ▲ | 6% | ▲ | 22%
    Demand
Demand for Steam Turbines will rise by 6.2% over the next two years, and by 31% by 2020 Q2, driven by Asian power utility capital expenditures and underlying Asian industrial growth, and more balanced global growth between 2015 and 2020.
The current steady demand growth rate of 0.7% per quarter (3.2% per year) will continue for the next two years (through 2015), driven mostly by Asian investment in power generation plants. It will accelerate gradually in 2015 and beyond to 1.1-1.2% per quarter, as American and European power investments return in response to gradually improving economies and reduced uncertainty around government policies toward emissions and renewable energies.
Utility spending in Asia will continue its strong growth path.
      Asian power sector capital spending will grow by 8% in 2013, as power plants take deliveries from previous orders.
o Indian utility Reliance Power and the Gujarat State Electricity Corporation are taking delivery of orders worth approximately $1b (orders were originally placed in 2011). Reliance Power ordered steam turbines as part of a $750m contract for a
2.4 GW expansion of its Samalkot power plant. Gujarat State Electricity ordered power plant equipment worth $250m for a 375 MW plant. These are just two examples of 5 GW in power projects underway in Tamil Nadu, Orissa, Andhra Pradesh, and Bihar.
In China, power plants are adding more than 3.2 GW in output, for example in Huating, Chongxin and Puqi.
Elsewhere in Asia, similar mega projects have been awarded and are deliveries are being taken in Pakistan, Vietnam, and Malaysia.

## Slide 41
The growth in Asian power industry capex will accelerate to 12-13% in 2014 and 2015, as Vietnam takes delivery of steam turbines for its nuclear plants and Russia builds infrastructure to support its aggressive nuclear power program. Asian nuclear plants represent over 60% of the world’s planned 200 GW in nuclear capacity.
  Vietnam is restructuring its electric power sector to address growing concerns about power reliability. As a result, Vietnam is building eight nuclear power plants, with construction scheduled to begin next year (in 2014). The massive $20 billion project is anticipated to produce 4 GW when finished.
  In Russia (considered ‘Asia’ here to differentiate it from the starkly different Western European demand pattern), although most of the nuclear power plants will be more toward Europe), 10 large reactors are under construction and seven replacement plants are planned, which will result in new steam turbine orders over the next two years. By 2016 ten new reactors totaling 10 GW should be operating.
Power projects in India and the Middle East will fuel growth of capex of 10-11% in the 2016-2020 timeframe.
In India, Adhunik Power & Natural Resources is building 3.5 GW in new power generating capacity. The company plans to set up 1.2 GW power plants in Bihar and Chhattisgarh, and is in the process of doubling the capacity of its 540 MW power project at Jamshedpur (it has so far taken delivery of one of two 270MW units for its coal fired thermal power plant).
Indian Railways is building a 1.3 GW supercritical power plant at Adra in West Bengal.
In the Middle East, the UAE will build four nuclear reactors of 1.4 GW each, and Turkey will invest $20b in six 1.4 GW reactors. The projects will take 10 years to complete.
Utility capital spending in the US is rising at about 4% per year, a rate that should stay steady from now through 2020. Environmental regulations in the US and Europe are slowing orders for coal- fired steam turbines. In March and April 2013, the US legislature finalized the long-pending Clean Air Transport Rule and the Utility MACT (Mercury Air Toxin) rules, imposing stricter emission standards and requiring expensive retrofits for existing coal-fired plants. Complying with these rules will cost US power companies up to $18b per year, according to the US-based National Economic Research Associated (NERA), so in order to avoid some of the compliance costs, US utility AEP plans to retire nearly 6 GW in coal-fired generation capacity, while retrofitting emission controls on the remaining ones over the next ten years (at a cost of $6-8b). These increased costs are slowing US investments in coal-fired power plants, and hence the purchase of steam turbines and other power sources. Government incentives to promote renewable energy sources like wind and solar power has also stymied steam turbine demand in the US. However, the US regulations have been short-term (up for annual renewals) and politically volatile (as evidenced by the tortuous revision of the Production Tax Credit in 2012 Q4 and 2013 Q1).

## Slide 42
Utility spending in EMEA is rising at 3% in 2013, and 1% in 2014, but will pick up to 4-5% per year in 2015-2020. The German government increased its 2020 target from 20% of energy from renewable energy sources to 30%, which will dampen Steam Turbine purchases.
Across the European Community, emissions directives and nuclear phase-out has temporarily restrained demand for steam turbines.
  The European Commission’s Industrial Emissions Directive (IED) (proposed in 2010) will also limit emissions. The response was immediate: Hitachi’s list of new steam turbine orders from Europe shrank by 50% YOY in 2011 Q1, as utilities
shifted their plans toward gas-fired and renewable power generation capacity instead of coal-fired units.
  Following Japan’s nuclear calamity, EU countries re-evaluated their nuclear power
programs, slowing new orders for nuclear steam turbines. Germany shut down at least seven nuclear power plants and plans to abandon nuclear power entirely. The Swiss government abandoned plans to build new nuclear reactors pending further review. Italy has halted any decisions and research into suitable locations for nuclear sites.
Project sponsors and equipment manufacturers are focusing on equipment that conforms to the stricter emissions standards. Some projects are proceeding, especially those that began several years ago, for example:
  Grosskraftwerk Mannheim, a coal-fired cogeneration plant in Germany with an installed base of 1.67 GW ordered two 900 MW steam turbines and boilers to
replace the current 220 MW turbines for delivery in 2013. The original contract was signed with Alstom in 2009.
  Slovenian utility Termoelektrarna is constructing a 600MW coal-fired steam power plant in northeast Slovenia, slated for completion next year (in 2014). The original plan was announced in 2009.
  UK utility Bioflame ordered steam turbines from Siemens for a new plant that will
run on waste wood.
  Ireland’s Electricity Supply Board also ordered steam turbines for the Poolbeg combined cycle plant near Dublin. Czech power utility CEZ placed a $52m order with Skoda Power, the largest domestic order in ten years for Skoda.
Industrial production, an indirect driver of demand for power, will gallop in Asia over the 2013-2020 timeframe. Exhibiting a similar pattern to demand in the power sector, industrial growth in Asia will increase from 8-9% in 2013 to 13% in 2014, before tapering to 10% over the 7-year period through 2020. In contrast, industrial production in the US will grow at only 2.5% in 2013, then rise gradually to 5-6%/year by 2020. In Europe it will stagnate until 2016, when it will pick up to 4-5%/year.

## Slide 43
Low natural gas prices will help to keep buyers interested in purchasing steam turbines, although their impact is subordinate to the influence of regulatory mandates. While gas prices will rise by 7% in 2013, prices are low by historical standards, and they are projected to fall again by 2-6% per year over the next 3 years as gas exploration ramps up worldwide and increase supply dramatically, before rising at 1-3% per year between 2017 and 2020.
Figure 12: Demand for Steam Turbines
    Supply (Capacity)
Siemens, MHI, Doosan, and Toshiba are adding capacity to focus on growing Asian and Eastern European markets, but uncertain demand growth due to environmental regulations and nuclear plant safety concerns are restraining capacity investments. Utilization rates will rise from 88% in 2013 to 92% in 2016 as a result, giving suppliers pricing power.
The top Steam Turbine manufacturers are:
      Siemens (Germany)
      Alstom (France)
      GE (US)
      Ansaldo (Italy)
      BHEL (India)
      MHI (Japan)
      Shanghai Electric (China)
      Hitachi (Japan)
      Doosan (Korea)
      Toshiba (Japan)
Capacity additions in 2012 H1 more than kept up with demand growth, pushing industry utilization rates down from 88% in 2011 to 86% in 2012 Q2.
4,000
3,000
8,000
7,000
6,000
5,000
2,000
1,000
-
05 Q106 07 08 09 10 11 12 13 14 15 16 17 18 19 20
Sales in
Nominal Dollars ($M US)
Asia
EMEA
Americas

## Slide 44
Siemens completed a 17k square meter expansion at its Vadodara, India plant in 2011 Q4, tripling the plant’s capacity. It added three production bays, 200 workers, and the capability to manufacture steam turbines with output up to 150 MW. The plant also makes compressors, which benefitted from the expansion as well.
Hitachi opened a new $600m plant near Chennai, India in 2012 Q1, with capacity for 4 GW of new equipment annually.
Chennai-based BGR Energy Systems entered the super-critical steam turbine segment by investing $1b in two manufacturing facilities in Tamil Nadu, India, 70% of the of which will support capacity for steam turbines (the remaining 30% will be for generators). The plants began manufacturing operations in 2012, and shipped their first units in 2013 Q1.
Siemens opened a new plant to make steam turbines in Badung, Indonesia in June 2012. The $13m plant is a joint venture with local partner Nusantara Turbin and Propulsi. It has capacity for up to 60 SST-140 steam turbines per year, units for mechanical drive applications with power ratings of up to 20 MW. The plant is primarily an assembly operation, and has been built to comply with Indonesia’s local content regulations, which require 40% local content. The plant is intended to meet orders primarily from the local textile and sugar industries, but is capable of supplying units for oil & gas applications as well.
Subsequent demand growth has outpaced these capacity additions, however. New regulations on coal-fired power plants (discussed in the demand section) and concerns over nuclear power plant safety after the Fukushima plant meltdown have discouraged further major capacity investments. Alstom is actually cutting back capacity for nuclear steam turbines due to a lack of orders. It laid off 80 workers at its Chattanooga turbine factory in March 2013. The bulk of these employees worked on Alstom’s ARABELLE™ steam turbines for nuclear applications.
Figure 13: Capacity Margin - Steam Turbines
90%
110%
$800
$700
$600
$500
$400
$300
$200
$100
$0
13 Q1 14
17
18 19
20
Utilization
Rate
70%
50%
Capacity Margin (Nominal
$M USD
per Quarter)
15 16
Capacity Margin
Utilization Rate

## Slide 45
Beginning in 2012 Q3, industry utilization rates began to rise again, reaching 88% in 2013 Q1. They will reach 90% in 2014 Q1 as few manufacturers add more capacity. Capacity Margin will shrink gradually from $740m to $600m over the same period.
Doosan has the most available capacity of any major supplier at a utilization rate of 80%, after major capacity investments in China in 2011.
Siemens and Alstom are both 85% utilized on average, slightly lower than the industry average due to their large scale of operations and ability to re-task workers and machinery as needed between turbine manufacturing operations.
GE is 85% utilized in China, where it has also expanded recently, and 90% utilized in the US.
MAN is 90% utilized, citing new orders from oil & gas and manufacturing industry customers, in conjunction with no new steam turbine capacity investments for two years.
Ansaldo is also 95% utilized in 2013 Q2, up from 80% in 2010. Financial troubles at its parent company, Finmeccanica, have prevented the supplier from investing in new capacity, and it will soon be 100% utilized.
Elliott (Ebara) is 95% utilized after a long stretch with no steam turbine capacity investments due to uncertain economic conditions.
Table 10: Reported or Estimated Capacity Utilization Rates at Selected Steam Turbine Suppliers
Company | Country | Current Level | 12-Month Forecast
Alstom | China | 85% | 85%
Ansaldo | Italy | 95% | 100%
Doosan (Skoda) | Czech Republic | 85% | 85-90%
Doosan (Skoda) | China | 80% | 80%
Elliott (Ebara) | US | 90% | 95%
Elliott (Ebara) | Japan | 95% | 95%
GE | US | 90% | 90%
GE | China | 85% | 85%
MAN | Germany | 90% | 95%
MHI | Japan | 95% | 95%
Siemens | US | 85% | 85-90%
Siemens | Germany | 80-85% | 85%
TGM Kanis | Brazil | 88% | 90%

## Slide 46
MHI is expanding steam turbine capacity in China and Singapore in 2013, the only supplier with major expansion plans this year, pursuing a regional strategy to lower its manufacturing cost base and gain greater access to other markets in the Asia-Pacific region.
In China, MHI established Mitsubishi Heavy Industries Jieneng (Qingdao) Steam Turbine Co., Ltd., in conjunction with Qingdao Jieneng Steam Turbine (Qingdao), in January 2013. Qindao is an established manufacturer of steam turbines with output of 60 MW or less for the Chinese market, typically producing about 500 turbines per year. MHI is investing $65m in the JV, which will manufacture steam turbines with output of 50-100 MW for local industrial and oil & gas applications. MHI hopes to gain greater access to the Chinese market and to expand its access to low-cost manufacturing through this JV. The new capacity will come online in late Q3 or early Q4.
In Singapore, MHI established Mitsubishi Heavy Industries Engineering & Services Private Ltd. (MIES), investing $27m in new capacity for steam turbines used in oil & gas, chemical, and marine industry applications. The move expands existing operations, and will increase local manufacturing capabilities from units with a maximum output of 120 MW to units with a maximum output of 200 MW.
The increase in utilization rates this year will push lead times up and give suppliers additional
pricing leverage in negotiations.
Lead times for the smaller reference unit (50 MW) are currently 11-12 months, and lead times for the larger one (120 MW) are 16-18 months. Planning cycles for refineries and power plants are long enough to accommodate these lead times levels presently, but the last time utilization rates were
above 90% (in 2009), lead times were more than 16 months for the smaller units and as much as two years for the larger one.
Planned capacity additions will not keep up with continued demand growth, and industry utilization
rates will reach 92% in late 2016 at current patterns of demand and capacity growth. Only two
relatively minor suppliers have large capacity addition plans over the next two years, which will add only about 5 GW in annual equipment output capacity – compared to projected demand growth of 16 GW in India alone.
Doosan is in the planning stages for an expansion at a Skoda plant in the Czech Republic (Doosan bought Skoda in 2009). The new unit will serve the combined-cycle market when it comes online in Q2 or Q3 next year, with capacity for 10-12 units with output ratings from 120-280 MW.
Toshiba is expanding capacity for supercritical steam turbines in India, in conjunction with local partner JSW. Its plant in Chennai currently manufactures 500-1,000 MW steam turbines, with eight production bays turning out 3-6 turbines per year. The expansion, due for completion in 2015, will double the plant’s capacity to approximately $400m in annual equipment value. It will double headcount as well, to approximately 500 workers. The firm

## Slide 47
anticipates that all of the new capacity will be absorbed by orders from India, where it is relying on projections of demand for 16 GW in new thermal generation capacity every year until at least 2017.
Figure 14: Demand vs. Capacity - Steam Turbines
    New contracts
Combined cycle orders, for new plants and retrofits, dominated new contracts awarded in the relevant turbine output ranges. The contract awards are highly concentrated among the top three suppliers: Siemens, Alstom, and GE.
Siemens, Alstom, and GE won most of the contract awards in the relevant output ranges for delivery from 2012 onward. These suppliers have the most capacity available and the lowest lead times, giving them an advantage over more heavily-utilized competitors. GE signed a memorandum of understanding (MOU) with Toshiba in January 2013 to jointly develop more efficient steam turbines for combined-cycle applications, which will make it even more competitive bidding for these contracts. The agreement stems from the firms’ joint work on the Nishi Nagoya Power Plant in Japan, which is targeting 62% thermal efficiency when it is completed in 2014. This would be the highest efficiency of any combined-cycle plant currently operating (the current record is 61%). Given utilities’ gravitation toward any increase in efficiency, this partnership could significantly strengthen both suppliers’ competitive position.
Their contracts include (in order of overall contract value):
      GE booked an order for the largest combined cycle plant in India in 2010, a $750m contract that includes all plant equipment for the three generating units at Reliance Power’s Samalkot power plant. The agreement covers six 9FA gas turbines (260 MW each), three
D-11 Steam Turbines (288 MW each), as well as mechanical and electrical auxiliaries and a 15 year service agreement. By bundling this much equipment together with a long term service plan, at pricing levels accepted in the Indian market, Reliance achieved a 35%
100
160
140
120
15
16
17
18
19
20
Capacity
Demand
Index
(2009
48
Q1=100) 80
60
40
13 Q1 14

## Slide 48
49
discount over prevailing prices for 2010 (about $350m per plant). The units entered full commercial operation in 2012 Q4.
Siemens booked an order for three steam turbines along with the three SGT6-8000H gas turbines ordered by Florida Power and Light in 2012 Q4. The 150 MW units cost $18.7m each ($56m total), after a net 15% discount for economies of scale (ordering three units together) and economies of scope (ordering the combined cycle plant with associated gas turbines, generators, controls, etc.)
Alstom sold a 240 MW steam turbine to Irish utility ESB as part of the Carrington power station, due for delivery in 2016. Net of bundling discounts, the unit cost approximately
$32.4m.
Alstom booked an order for two combined cycle units from Indian IPP GVK Industries in 2010 (with final delivery scheduled for this year). The steam turbines for the units sold at almost a 30% discount, net of “country pricing,” economies of scale, and bundling discounts due to the size of the package awards. The contract totaled $590m for two full CC units (total output of 800 MW) including two gas turbines, two steam turbines, HRSGs, generators, balance of plant, civil works, and a 10-year LTSA.
GE also sold two SC5 steam turbines to Emirates Aluminum (EMAL) as part of a combined cycle plant. The 100 MW units, designed for lower pressure steam than most power plants, sold at a modest 5% discount due to economies of scope with the other power plant equipment.
Baotou Iron & Steel ordered two combined cycle plants in 2012 Q3 to generate power from blast furnace gas created by its steelworks in Baotou City (Mongolia). MHI and Dongfang Turbine will supply one 50 MW steam turbine each (Dongfang under license from MHI). Net of discounts for bundling the steam turbines with the rest of the power plant equipment and migrating much of the manufacturing to Dongfang’s facilities in China, the units cost approximately $5.6m.
Siemens will supply two gas turbines, a steam turbine, three generators, electrical equipment, and the ancillary and auxiliary systems for the Wang Noi plant, for the Electricity Generating Authority of Thailand (EGAT). The 270 MW steam turbine for the power sold for
$20m, including substantial discounts off “list” for Thailand’s low pricing expectations (25%) and a 10% discount attributable to economies of scope for the large package award –
$500m in electrical machinery for the Wang Noi and Chana power plants. EGAT ordered the equipment in August 2011 and final delivery is scheduled in 2014 Q2.
GE booked an order for two gas turbines, one steam turbine, and three generators from Turkey’s Tupras in 2012 Q4. The steam turbine made up about $11m of the overall package, accounting for price reductions of about 25% due to a combination of the size of the overall order, pricing level expectations in Turkey, and Tupras’ attractiveness as a customer. Tupras is Turkey’s largest refiner and part of the KOC group, the country’s largest company.

## Slide 49
59
Siemens and GE booked major contracts to convert simple-cycle plants to combined-cycle operation. Both of the orders follow the contracts for the gas turbines by 1-2 years foregoing bundling discounts the buyer could have achieved by ordering the equipment together.
Siemens booked orders for steam turbines to convert two simple cycle power plants in Argentina to combined cycle operation in October 2012. The first order is for a 280 MW unit, destined for the Ensenada de Barragán plant, near Buenos Aires. Under the contract, Siemens will furnish one SST5-5000 steam turbine, one SGen5-1000A generator, two heat recovery steam generators, and the SPPA-T3000 instrumentation and control system. The second order, for the Brigadier López power plant in Santo Tomé, includes one SST-900 reheat steam turbine, one SGen5-100A generator, one heat recovery steam generator, and the SPPA-T3000 instrumentation and control system. Together, the steam turbines cost approximately $44.5m.
GE won a $200m contract from Saudi Electricity Company (SEC) to convert its Riyadh PP10 power plant to combined cycle. The conversion will add more than 50% to plant capacity (from 2,200 MW to 3,500). The power plant currently features 40 GE frame 7EA gas turbines. GE will provide 10 SC series steam turbines under the contract, along with control systems, mechanical and electrical auxiliaries, and installation services. After a discount off list of approximately 20% to account for the large order and its integration with controls and auxiliaries, the unit cost of the turbines is approximately $14m. GE began shipping the equipment in 2013 Q1, and will continue deliveries through most of 2014.

## Slide 50
Table 11: Summary of New Contracts and Estimated Values for Steam Turbines
Buyer | Country of Installation | Supplier | Product | Estimated Value ($m) | Estimated Cost/Unit ($m) | Cost per kW
SEC | Saudi Arabia | GE | 10 units, 130 MW | $140 | $14.0 | $108
SEC | Saudi Arabia | Alstom | 2 units, 342 MW | $68 | $34.1 | $100
Reliance Power | India | GE | 3 units, 288 MW | $65 | $21.6 | $75
Cairo Electricity | Egypt | Ansaldo | 2 units, 280 MW | $58 | $29.0 | $104
FPL | USA | Siemens | 3 units, 150 MW | $56 | $18.7 | $125
Isolux Engeneria | Argentina | Siemens | 2 units, 280 MW | $44 | $22.2 | $106
3S Enerji | Turkey | Skoda | 3 units, 133 MW | $41 | $13.7 | $103
TransAlta | Canada | MHI | 1 unit, 250 MW | $36 | $35.6 | $142
ESB | Ireland | Alstom | 1 unit, 240 MW | $32 | $32.4 | $135
GVK Industries | India | Alstom | 2 units, 100 MW | $30 | $15.2 | $153
Abener Energía | Mexico | Toshiba | 1 unit, 242 MW | $25 | $25.0 | $104
EMAL | UAE | GE | 2 units, 100 MW | $24 | $12.0 | $120
EGAT | Thailand | Siemens | 1 unit, 270 MW | $22 | $22.1 | $82
Amazonas Distrib. | Brazil | Siemens | 1 unit, 200 MW | $21 | $20.8 | $104
Public Utility | Syria | Ansaldo | 1 unit, 100 MW | $14 | $13.7 | $137
Bangladesh Power | Bangladesh | Hyundai | 1 unit, 135 MW | $13 | $13.4 | $99
Baotou Iron & Steel | China | MHI | 2 units, 50 MW | $11 | $5.6 | $112
Tupras | Turkey | GE | 1 unit, 100 MW | $11 | $11.0 | $110
Enel | Italy | Ansaldo | 3 units, 20 MW | $11 | $3.5 | $175
Xstrata | Australia | Siemens | 1 unit, 45 MW | $7 | $6.7 | $148
Mondi | South Africa | TGM Kanis | 1 unit, 48 MW | $6 | $6.0 | $125

## Slide 51
5.2 Analysis
5.2.1 Costs
Global cost levels will rise 1.7% in 2013, and a total of 16% from 2013 Q2 to 2020 Q2, driven by increasing Asian labor costs and slow cost growth for underlying steel and component costs.
Similar to the cost structure for Gas Turbines, metals and metal components make up the largest part of the cost to manufacture Steam Turbines, at 54% of the total. Steam turbines contain a lower percentage of advanced alloys than gas turbines, relying more on carbon steel and stainless steel, although the rotor is typically nickel-chrome-molybdenum-vanadium alloy. Most manufacturers buy the blank rotor (without blades) and the casing from forges and foundries, respectively.
Labor costs are another 30% of the overall cost structure. Production labor represents 12% of the total, including skilled welders, machine operators, crane operators and shop hands. Management and engineering labor is 10% of the total, proportionally less than for gas turbines because steam turbines do not require engineering design for the combustors or onboard electrical system.
Benefits such as training, bonuses, pension plans, and health care round out the total for labor at approximately 6% of the overall cost.
Energy costs account for 7% of the overall cost structure. Much of the manufacturing process for a steam turbine requires large amounts of heat and electricity. For example, the rotor must first be heated and forged, welded with overlays, heat treated, and welded to the blades.
Figure 15: Cost Structure for Steam Turbines
Note: Prices are ex-works.
140 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
120 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
100 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Manufacturing |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cost | 80 |  |  |  |  |  |  |  |  |  |  |  |  | 
Breakdown |  |  |  |  |  |  |  |  |  |  |  |  |  | 
(2006 Q1=100) | 60 |  |  |  |  |  |  |  |  |  |  |  |  | 
40 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
20 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
06Q1 07 |  | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Chemicals & Plastics Benefits Production Labor |  |  |  | Electronics Other Materials Machinery and Parts |  |  |  |  |  |  | Energy Professional Labor Metals |  |  | 

## Slide 52
Overall costs were practically stable in Q1, flat costs in the Americas and EMEA counterbalanced a 0.5% increase in Asia, mostly driven by rising wages and salaries for welders and engineers.
Labor costs, particularly in Asia where manufacturers are still expanding capacity, will be the biggest driver of cost growth going forward. Welders and engineers are in short supply compared to demand, and cost of living increases are contributing to quarterly labor cost growth of 1% in Asia, compared to half a percent or less in the other two regions. Energy costs, rising at an average annual rate of 2-3%, will help drive cost growth, while underlying steel costs will rise slowly and gradually.
Driven by the above factors, overall costs will increase 2-5% annually through 2020, for a total increase of 16% by 2020 Q2. Asian cost levels will rise fastest at 18%, driven by the comparatively fast growth for labor costs. Overall cost levels will rise 13% in the Americas, and 11% in EMEA, where slow economic growth will restrain cost increases for labor and some materials.
    Profit Margins
Steam Turbine manufacturers earned average operating margins of 8.5% in 2012, lower than gas turbines due to the comparatively low level of engineering labor required.
The supplier list for Steam Turbines is highly congruent with the one for Gas Turbines, and most manufacturers make the units in the same operating divisions, making the margin levels difficult to separate.
Margins are lower for steam turbines than for gas turbines. GE and Alstom indicated that their margins are up 2-3 percentage points lower for these units, while Siemens, the market leader, makes about one percentage point less. There are two reasons for the difference in margins:
      There is less engineering labor involved in the design of Steam Turbines (as a percentage of the total cost), due to the absence of complexities of combustion technology and as many superalloys, and because the technology is not updated as often.
      Steam turbine technology is more nature, and while metallurgy, valves, and sealing technology are still subjects of occasional technological improvements, the upgrade cycles and efficiency gains are less frequent. As a result, suppliers are less able to mark up the price. In contrast, gas turbine models are updated almost constantly, with and standard upgrade packages developed for older units. For example, Alstom’s GT26 has a 2006 version and a 2011 version, indicating a 5-year design overhaul cycle.
Margins typically increase with unit size, due to the higher level of technology and the shorter list of competitors. As steam pressure increases, so does the complexity of the rotor, blade, and valve metallurgy and design, allowing the supplier to bill a higher percentage of engineering labor. In addition, manufacturers that only make smaller units, such as Dresser Rand, Kawasaki, and Triveni, do not compete for units over 120-150 MW, reducing the number of competitors on equipment tenders. The market leaders indicate that margins for units rated above 150 MW are 2-3 percentage

## Slide 53
price growth will amount to 22% by 2020 Q2, 6% higher than cost increases.
points higher than smaller units, and large steam turbines (with output over 500 MW) are another 2- 3% more profitable.
The same regional pattern applies with Steam Turbines as with Gas Turbines, with Japanese suppliers making markedly less (3-4% vs. 6-18%) than their competitors in other regions.
Despite the slightly lower percentage of margin, accelerating demand growth and tightening capacity utilization will give suppliers more bargaining leverage on prices, and Steam Turbine prices will rise about one percentage point faster than costs through 2020, indicating average margin growth of six percentage points for Steam Turbine manufacturers.
  Prices
Prices will rise a total of 22% by 2020 Q2, driven up by increased supplier pricing leverage as capacity utilization rates rise to 92%.
Average prices for the reference units covered in this study are $11.7m. This covers a range of equipment from 50-120 MW, however, with a difference of $9m in average unit cost between the two. The reference units and prices at benchmark levels in the US are listed below. These reference prices are for the turbine alone, excluding components such as an HRSG (Heat Recovery Steam Generator) or an electrical generator, to eliminate the impact of regional packaging differences and different auxiliary component options.
    Reference unit 1:
      50 MW steam turbine for refinery or chemical plant mechanical drive with steam pressure rating of 140 bar.
      Price: $7m
    Reference unit 2:
      120MW steam turbine with single reheat for combined cycle power generation with steam pressure rating of 140 bar.
      Price: $16.3m
Global prices rose by just under 1% in 2013 Q1, driven by the combination of rising demand and rising capacity utilization rather than cost increases. Prices will increase a total of 3% this year, almost twice as fast as costs due to the abovementioned tightening of capacity utilization. Siemens
in particular is eager to amortize capacity investments last year and is pushing for price increases of
as much as 5% this year. In contrast, MHI is holding prices steady (despite its own capacity
investments), taking the position that building volume will be the best way to make back its investment. It can afford to adopt this strategy because it invested in joint ventures to build capacity, rather than taking the financial burden on its own.
Price increases will accelerate slightly to 3.5% in 2014 and 2015 as Capacity Margin continues to tighten, then slow to 2.5% annually starting in 2016 as utilization rates stabilize at 92%. Cumulative

## Slide 54
1 Shanghai and Dongfang Electric primarily supply steam turbines for coal-fired power plants in China, with MW ratings well above the levels of either reference unit priced in this study (600-1,000 MW).
Figure 16: Overall Price Forecast for Steam Turbines
16
14
12
10
Cost
per 8 Unit ($m)
6
4
2
-
2004 2006 2008 2010 2012 2014 2016 2018 2020
Min Global Average Max
The same regional pricing dynamics described in the Gas Turbines Chapter apply to Steam Turbines. Manufacturers’ final price quotes are determined in large part by the region of the end- user, rather than any actual regional cost differences in manufacturing. Manufacturers such as Bharat Heavy Electricals Limited (BHEL), Shanghai Electric, and Dongfang Electric1, are exceptions to this maxim, but these firms rarely sell units outside of their home countries. For example, 89% of Shanghai Electric’s overall sales were to China in 2011 ($9.6b out of $10.8b). This reinforces the necessity for global manufacturers selling in these regions to meet local price levels, but does not apply competitive pressure in higher cost environments such as North America or Western Europe.
The regional price differentials are similar to those for Gas Turbines. Also similar are the ways that manufacturers bring down manufacturing costs to protect margins. They can use lower-cost materials, as well as less costly valves, package components, and blade technology, along with cutting custom engineering. Examples of regional pricing include:
When MHI sold a steam turbine to Baotou Iron & Steel, it priced the unit roughly 20% below US levels - $8m instead of $10m.
GE and Alstom both made major sales to buyers in India (Reliance Power and GVK Industries, respectively). After isolating other variables such as economies of scale and bundling discounts, the steam turbines sold for 15-20% less than benchmark levels.
55

## Slide 55
When TGM Kanis sold a 48 MW turbine to South African paper producer Mondi, it marked the price of the unit down slightly (approximately 5%) from typical price levels in Brazil, which are already 10% lower than US price levels.
Siemens sale of a combined-cycle steam turbine to EGAT in Thailand carried an 18% regional pricing discount, as well as a discount of approximately 5% for bundling the steam turbine with the gas turbine and plant package.
Table 12: Regional Price Variations over Time for Steam Turbines Compressors
Region/Country | Today | 2014 | 2015 | 2020
North America | 1.00 | 1.00 | 0.99 | 1.08
Latin America | 0.90 | 0.94 | 0.97 | 1.14
Europe | 1.04 | 1.07 | 1.07 | 1.15
Africa* | 0.85 | 0.87 | 0.86 | 0.95
India | 0.83 | 0.84 | 0.85 | 0.99
Russia | 0.85 | 0.89 | 0.90 | 1.06
China | 0.80 | 0.81 | 0.80 | 0.88
Japan | 1.10 | 1.12 | 1.12 | 1.16
Other Asia | 0.90 | 0.91 | 0.92 | 1.00
Notes:
“*” means supplied by foreign manufacturers only
5.3.1 Price Differences by Technology, Model, and Feature
Output rating determines the size of the steam turbine, and has the most impact on unit cost. Cost per kW falls with higher output ratings.
For the smaller reference unit, a 50 MW unit used for mechanical drive, costs move in a linear pattern as power rating increases or decreases. A 30 MW unit costs approximately $1.82m less than a 50 MW unit ($5.2m) at 140 bar steam pressure, and a 70 MW steam turbine costs roughly
$1.82m more ($8.8m). Manufacturing economies of scale are not typically realized for units in this size range because casing thickness and rotor metallurgy to cope with higher internal temperatures scale up directly with output.
For the higher MW range, 100-140 MW, the steam turbines use a dual casing to handle higher pressures. This causes a step change in unit cost but allows an increase in economies of scale for a single unit because only the first casing needs to be thicker to handle higher steam pressures. As a result, increases in unit cost slow as the power rating increases. A 120 MW unit costs $2.6m more than a 100 MW turbine, and a 140 MW machine costs $2.4m more than one rated for 120 MW.

## Slide 56
Table 13: Incremental Cost per Extra Parameter or Feature for a 30-70 MW Steam Turbine for Mechanical Drive
(based on the reference unit specified above)
Parameter or Feature | Unit of Measure | Indicative Cost Impact | Notes / Comments
Output Power Rating | MW (50 MW as reference point) | Reducing turbine output rating from 50 MW to 30 MW reduces unit cost by $1.82m. Increasing power rating to 70 MW raises unit cost by $1.82m. | Cost increases are linear for units in this range, as materials and engineering costs scale up directly with the larger turbine sizes.
Steam Pressure | 140 bar at 50 MW as reference point | Reducing pressure rating from 140 bar to 120 bar cuts unit cost by $1.6m. Increasing it to 160 bar costs only $0.65m more. | Cost increases slow rapidly with steam pressure increases for smaller turbines due to the comparatively small internal diameter of the turbine, which necessitates a smaller increase in casing thickness with steam pressure.
Cost per kW Installed | $140 as reference point (50 MW unit at steam pressure of 140 bar) | Increasing unit output from 50 MW to 70 MW reduces cost per kW from $140 to $126. | Cost per kW falls rapidly for steam turbines in this range due to the dramatic increase in unit efficiency (smaller units are markedly less efficient).
Note: Changing one parameter usually changes others, and cost impact may not be additive or linear.
Prices do not include steam turbine package components such as HRSG, electrical generator, support structures, or exhaust stacks. This facilitates a direct comparison between turbine costs, eliminating multiple components that are either outsourced (made by a different manufacturer and packaged by the turbine supplier) or excluded entirely from some contracts.

## Slide 57
Table 14: Incremental Cost per Extra Parameter or Feature for a 100-140 MW Steam Turbine for Combined-Cycle Power Generation
(based on the reference unit specified above)
Parameter or Feature | Unit of Measure | Indicative Cost Impact | Notes / Comments
Output Power Rating | 120 MW as reference point | Reducing turbine output rating from 120 MW to 100 MW reduces unit cost by $2.6m. Increasing power rating to 140 MW only raises unit cost by $2.37m. | For turbines in the combined- cycle plant range, cost increases slow as the size of the unit increases because incremental power output can be achieved by adding another stage to the turbine, instead of scaling the entire unit up.
Steam Pressure | 140 bar at 50 MW as reference point | Reducing pressure rating from 140 bar to 120 bar cuts unit cost by 1.3m. Increasing it to 160 bar costs an additional $1.2m. | The deceleration of cost increases with steam pressure is slower for larger steam turbines due to the higher base material costs associated with the dual casing.
Cost per kW Installed | $140 as reference point (50 MW unit at steam pressure of 140 bar) | Increasing unit output from 120 MW to 140 MW reduces cost per kW from $136 to $133. | As with steam pressure, cost per MW falls more slowly with power rating for the larger turbines due to the higher material costs associated with the larger units.
Note: Changing one parameter usually changes others, and cost impact may not be additive or linear.
Higher steam pressures correlate with higher turbine costs, as higher pressures require thicker casings and more heavily-specified control valves. This cost increase is linear for the larger reference unit, as the volume of material increases for both casings with rising steam pressure, compared to only the one casing for the smaller reference unit.

## Slide 58
Figure 17: Steam Turbine Cost vs. Power Output by Application and Steam Pressure
Economies of scale benefits for ordering multiple units accelerate from the 70 MW unit to the 120 MW unit. This is because the larger turbine requires more engineering labor to begin with, which eliminates more cost if a buyer orders multiple units. It also eliminates more down-time for setups (and idle time between orders) on the more expensive cranes and cutting and milling machines
5.0
0.0
10.0
25.0
20.0
15.0
0
50
100
150
$m
Unit MW Rating
Cost per kW falls rapidly with power rating for the smaller reference unit, but more slowly for the combined-cycle steam turbine. For the smaller reference unit range it falls from $173 per kW at 30 MW to $126 per kW at 70 MW. Cost per kW increases for the combined-cycle unit, again because of the higher material costs for the dual casing and reheat capability, but still falls from $138 per kW to $133 per kW from power rating levels of 100 MW to 140 MW, respectively.
Figure 18: Steam Turbine Cost per kW Installed
Mechanical Drive - 120 bar
Mechanical Drive - 140 bar
Mechanical Drive - 160 bar
Combined Cycle
120 bar
Combined Cycle
140 bar
Combined Cycle
160 bar
80
60
40
20
0
200
180
160
140
120
50 100 150
$ per 100
kW
Unit MW Rating
Mechanical Drive - 120 bar
Mechanical Drive - 140 bar
Mechanical Drive - 160 bar
Combined Cycle - 120 bar
Combined Cycle - 140 bar
0
Combined Cycle - 160 bar

## Slide 59
used to make larger turbines. Economies of scale at the reference quantity of 10 units amount to a unit price discount of 10% for the smaller model, and as much as 15% for the larger model.
Figure 19: Economies of Scale in Steam Turbines
5.3.2 Should-Cost Analysis
Economies of scale are the most effective way for buyers to bring down unit costs, if their
requirements are large enough to merit ordering multiple units. On average, a buyer can get a
discount of 12.5% by ordering 10 units, or $1.5m at the average cost of the two reference units.
Economies of scope are the next most effective tactic, and the one most accessible for buyers that do not need to buy multiple units. Bundling the power turbine with the generator, HRSG, and package components, or the mechanical drive turbine with the turbomachinery it is driving can get discounts of up to 10%.
Value engineering can be used to reduce costs, but nearly always results in a concurrent reduction in turbine reliability. As a result, extensive cost reduction efforts by reducing specifications below those suggested by the application increases lifecycle cost. Nonetheless, some buyers have successfully reduced unit prices with the following tactics:
Reducing the amount of custom engineering for each turbine
Using less expensive valves, materials, and blade technology.
Using ”low-cost” manufacturing (e.g, Siemens’ new plant in Vadodara, India, GE’s partnership with Triveni (established in 2011), MHI’s JV investments in new capacity, and Doosan’s planned factory in the Czech Republic (see the capacity section for detail)).
Using ”low-cost” packagers (package components account for much of the difference in final contract prices)
$18
$16
$14
$12
$10
$8
$6
$4
$2
$-
0 2 4
8
10
12
Unit Cost ($m)
6
Units Ordered
50 MW
120 MW
60

## Slide 60
5.4 Price Negotiation Strategies
Combine steam turbine units in one order wherever feasible. Economies of scale are the most effective way to reduce unit costs, and can yield discounts of up to 15%.
Bundle steam turbine orders with as much other equipment as possible (gas turbines, boilers, HRSGs, generators, etc.) to get larger discounts from economies of scope (up to 10%).
Place orders or reserve capacity as soon as basic order parameters are identified. Accelerating
demand growth and rising capacity utilization are driving prices up by 2.5-3.5% annually, and placing orders early will avoid both price increases and potential lead time expansion.
Secure lead time guarantees on any orders with MHI or Ansaldo. Both suppliers are nearly fully utilized, and are at risk of dramatic lead time inflation.
11.7
0.6
0.0
1.5
1.2
0.0
8.5
2.0
-
4.0
6.0
8.0
10.0
Competitive bidding also yields cost reductions of 5% on average. This may seem lower than for some other equipment because Steam Turbine suppliers do not inflate “list prices” the way many manufacturers do when selling more commoditized equipment (e.g. valves). Most of the manufacturers know each other’s prices fairly well and do not want to lose sales by quoting prices
too high above those a competitor will offer, essentially building some of the benefit of competition into price quotes before actual bidding begins. In addition, manufacturers take the region of delivery into account when offering budgetary prices, to avoid being underbid by local suppliers.
Figure 20: Should-Cost for Steam Turbines
14.0
12.0
Base Cost
Competitive Bidding
Value Engineering
Economies of Scale
Economies of Scope
Supply Chain Integration
Should Cost
$m

## Slide 61
Reference product definitions and scope2
  Gas Turbines
    Reference unit 1:
      30 MW gas turbine used for mechanical drive on an EOR pump unit in field operation.
    Reference unit 2:
      70 MW gas turbine used for mechanical drive on a refinery pump or compressor, or small-scale simple-cycle power generation.
    Reference unit 3:
      240 MW gas turbine used for combined-cycle power generation.
  Steam Turbines
    Reference unit 1:
      50 MW steam turbine for refinery or chemical plant mechanical drive with steam pressure rating of 140 bar.
    Reference unit 2:
      120MW steam turbine with single reheat for combined cycle power generation with steam pressure rating of 140 bar.
2 The reference specifications below involve fewer detailed specifications than for some of the other equipment in this program since the overwhelming cost determinant of turbines is the output rating.

## Slide 62
7 Notes
The suppliers who were contacted directly for this study include, but are not limited to:
Alstom
Ansaldo
Doosan (Skoda)
Dresser-Rand
GE
Hitachi
Kawasaki
MAN Turbo
Mitsubishi Heavy Industries (MHI)
Pratt & Whitney Power Systems (part of MHI)
Rolls Royce
Siemens
Solar Turbines
TGM Kanis
Toshiba
Turbinen Technik
Vericor